## Slide 1: Computer Organization Principles
School of Software, Dalian University of Technology
Chi Lin (林驰)
chilin@mail.dlut.edu.cn

## Slide 2: Why do we need to study assembly language ?
Complicated
Boring
Tedious
Nearly useless
…

## Slide 3: Great Reality #2: You’ve Got to Know Assembly
Carnegie Mellon
Chances are, you’ll never write programs in assembly
  Compilers are much better & more patient than you are
But: Understanding assembly is key to machine-level execution model
  Behavior of programs in presence of bugs
    High-level language models break down
  Tuning program performance
    Understand optimizations done / not done by the compiler
    Understanding sources of program inefficiency
  Implementing system software
    Compiler has machine code as target
    Operating systems must manage process state
  Creating / fighting malware
    x86 assembly is the language of choice!

## Slide 4: Reason Two: Programmer Rankings
Higher Level Language yields Low Level Programmer.
Niubility = Familiar with ( or Grasp) Computer Principles + Data Structure + Algorithm + C/C++
Struggle ! You can be Niubility with no friends.

## Slide 5: Our Coverage
IA32
  The traditional x86
x86-64/EM64T (Optional)
  The emerging standard
Presentation
  Book presents IA32 in Sections 3.1—3.12
  Covers x86-64 in 3.13 (Optional)

## Slide 6: Chapter Four: Instruction Systems
Instruction Encoding (指令编码)
Addressing Modes and Formats (寻址方式)
Instruction Usage (指令使用方法)
RISC

## Slide 7: Chapter Four: Instruction Systems
Instruction Encoding (指令编码)
Addressing Modes and Formats(寻址方式)
Instruction Usage (指令使用方法)
RISC

## Slide 8: Chap 4.1 Instruction Encoding
Machine Instruction Characteristics
Types of Operands (操作数类型)
Types of Operations (指令操作种类)
Examples

## Slide 9: Chap 4.1 Instruction Encoding
Machine Instruction Characteristics
Types of Operands
Types of Operations
Examples

## Slide 10: Definition of Instruction Set(指令集)
The operation of the processor is determined by the instructions it executes, referred to as machine instructions or computer instructions.
The collections of different instructions that the processor can execute is referred to as the processor’s instruction set.

## Slide 11: Instruction Cycle State Diagram

## Slide 12: Elements of a instruction
Operation code: Specifies the operation to be performed (e.g., ADD, I/O). The operation is specified by a binary code, known as the operation code, or opcode.
Source operand reference: The operation may involve one or more source operands, that is, operands that are inputs for the operation.
Result operand reference: The operation may produce a result.
Next instruction reference: This tells the processor where to fetch the next instruction after the execution of this instruction is complete.

## Slide 13: Instruction Representation
Within the computer, each instruction is represented by a sequence of bits. The instruction is divided into fields, corresponding to the constituent elements of the instruction.
During instruction execution, an instruction is read into an instruction register (IR) in the processor. The processor must be able to extract the data from the various instruction fields to perform the required operation.

## Slide 14: Opcodes
Opcodes are represented by abbreviations. Common examples include
  ADD Add
  SUB Subtract
  MUL Multiply
  DIV Divide
  LOAD Load data from memory
  STOR Store data to memory
Operands are also represented symbolically. For example, the instruction

## Slide 15: High-Level Language To Low Level
X = X + Y (X=513, Y=514)
  Load a register with the contents of memory location 513.
  Add the contents of memory location 514 to the register.
  Store the contents of the register in memory location 513.
How to convert it into assembly language ?

## Slide 16: Turning C into Object Code
text
text
binary
binary
Compiler (gcc -S)
Assembler (gcc or as)
Linker (gcc or ld)
C program (p1.c p2.c)
Asm program (p1.s p2.s)
Object program (p1.o p2.o)
Executable program (p)
Static libraries (.a)
  Code in files p1.c p2.c
  Compile with command: gcc –O1 p1.c p2.c -o p
    Use basic optimizations (-O1)
    Put resulting binary in file p

## Slide 17: Compiling Into Assembly
C Code
int sum(int x, int y)
{
int t = x+y;
return t;
}
Generated IA32 Assembly
sum:
pushl %ebp
movl %esp,%ebp
movl 12(%ebp),%eax
addl 8(%ebp),%eax
popl %ebp
ret
Obtain with command
  /usr/local/bin/gcc –O1 -S code.c
Produces file code.s
Some compilers use instruction “leave”

## Slide 18: Data Types
“Integer” data of 1, 2, or 4 bytes
  Data values
  Addresses (untyped pointers)
Floating point data of 4, 8, or 10 bytes
No aggregate types such as arrays or structures
  Just contiguously allocated bytes in memory

## Slide 19: Instruction types
Data processing: Arithmetic and logic instructions.
Data storage: Movement of data into or out of register and or memory locations
Data movement: I/O instructions
Control: Test and branch instruction

## Slide 20: Number of Addresses

## Slide 21: Trade-offs of the number of addresses
More addresses
  Long execution time
  More complex program
  Faster (Register vs. memory)
  Flexibility
Fewer addresses
  More primitive
  Require a less complex processor
  Short length of instructions
Most computers employ a mixture of two- and three address instructions

## Slide 22: Instruction Set Design
One of the most interesting, and most analyzed, aspects of computer design is instruction set design.
The design of an instruction set is very complex because it affects so many aspects of the computer system. The instruction set defines many of the functions performed by the processor and thus has a significant effect on the implementation of the processor.
The instruction set is the programmer’s means of controlling the processor. Thus, programmer requirements must be considered in designing the instruction set.

## Slide 23: Instruction Set Design
Operation repertoire(操作种类): How many and which operations to provide, and how complex operations should be ?
Data types: The various types of data upon which operations are performed.
Instruction format: Instruction length (in bits), number of addresses, size of various fields, and so on.

## Slide 24: Instruction Set Design
Registers: Number of processor registers that can be referenced by instructions, and their use
Addressing: The mode or modes by which the address of an operand is specified

## Slide 25: Chap 4.1 Instruction Encoding
Machine Instruction Characteristics
Types of Operands
Types of Operations
Examples

## Slide 26: Types of Operands（操作数）
Machine instructions operate on data. The most important general categories of data are:
  Memory(内存地址)
  Register(寄存器)
  Immediate(立即数)

## Slide 27: Operands Forms

## Slide 29: Moving Data: IA32
Moving Data
  movl Source, Dest:
Operand Types
  Immediate: Constant integer data
    Example: $0x400, $-533
    Like C constant, but prefixed with ‘$’
    Encoded with 1, 2, or 4 bytes
  Register: One of 8 integer registers
    Example: %eax, %edx
    But %esp and %ebp reserved for special use
    Others have special uses for particular instructions
  Memory: 4 consecutive bytes of memory at address given by register
    Simplest example: (%eax)
    Various other “address modes”
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp

## Slide 30: movl Operand Combinations
Cannot do memory-memory transfer with a single instruction
movl
Imm
Reg
Mem
Reg
Mem
Reg
Mem
Reg
Source
Dest
C Analog
movl $0x4,%eax
temp = 0x4;
movl $-147,(%eax)
*p = -147;
movl %eax,%edx
temp2 = temp1;
movl %eax,(%edx)
*p = temp;
movl (%eax),%edx
temp = *p;
Src,Dest

## Slide 31: Simple Memory Addressing Modes
Normal (R) Mem[Reg[R]]
  Register R specifies memory address movl (%ecx),%eax
Displacement D(R) Mem[Reg[R]+D]
  Register R specifies start of memory region
  Constant displacement D specifies offset movl 8(%ebp),%edx

## Slide 32: Chap 4.1 Instruction Encoding
Machine Instruction Characteristics
Types of Operands
Types of Operations
Examples

## Slide 33: Assembly Characteristics: Operations
Perform arithmetic function on register or memory data
Transfer data between memory and register
  Load data from memory into register
  Store register data into memory
Transfer control
  Unconditional jumps to/from procedures
  Conditional branches

## Slide 34: Types of Operations (opcode)
The number of different opcodes varies widely from machine to machine. However, the same general types of operations are found on all machines. A useful and typical categorization is the following:
  Data movement
  Arithmetic & Logical
  State Control & Settings
  Jumping

## Slide 35: Data Movement Instruction

## Slide 36: Data Movement Instruction
Among the most heavily used instructions are those that copy data from one location to another. The generality of the operand notation allows a simple data movement instruction to perform what in many machines would require a number of instructions

## Slide 37: Data Transfer & Data Movement Instruction
The location of the source and destination operands must be specified. Each location could be memory, a register, or the top of the stack.
The length of data to be transferred must be indicated
The mode of addressing for each operand must be specified.

## Slide 38: Mov class
The instructions in the mov class copy their source values to their destinations.
The source operand designates a value that is immediate, stored in a register, or stored in memory.
The destination operand designates a location that is either a register or a memory address.

## Slide 39: Push & Pop
We add data to a stack via a push operation and remove it via a pop operation, with the property that the value popped will always be the value that was most recently pushed and is still on the stack.
First in last out

## Slide 40: Integer Arithmetic Operations

## Slide 41: Arithmetic Instruction
The execution of an arithmetic instruction may involve data transfer operations to position operands for input to the ALU, and to deliver the output of the ALU.
E.g. ADD %ESP, %EAX

## Slide 42: Logical Instruction

## Slide 43: Shift instructions

## Slide 44: Special Arithmetic Operations

## Slide 45: Comparison and Test Instructions

## Slide 46: Condition Code Register
In addition to the integer registers, the CPU maintains a set of single-bit condition code registers describing attributes of the most recent arithmetic or logical operation. These registers can then be tested to perform conditional branches. The most useful condition codes are:
CF: Carry Flag. The most recent operation generated a carry out of the most significant bit. Used to detect overflow for unsigned operations.
ZF: Zero Flag. The most recent operation yielded zero.
SF: Sign Flag. The most recent operation yielded a negative value.
OF: Overflow Flag. The most recent operation caused a two’s-complement overflow—either negative or positive.

## Slide 47: The Set Instructions

## Slide 48: Jumping Instruction
A jump instruction can cause the execution to switch to a completely new position in the program. These jump destinations are generally indicated in assembly code by a label.

## Slide 49: The Jumping Instruction/ branch Instruction

## Slide 50: Transferring Control
The call instruction has a target indicating the address of the instruction where the called procedure starts. Like jumps, a call can either be direct or indirect.
The ret instruction pops an address off the stack and jumps to this location. The proper use of this instruction is to have prepared the stack so that the stack pointer points to the place where the preceding call instruction stored its return address.

## Slide 51: Example of Nested Procedures (嵌套函数)

## Slide 52: Chap 4.1 Instruction Encoding
Machine Instruction Characteristics
Types of Operands
Types of Operations
Examples

## Slide 53: Using Simple Addressing Modes
void swap(int *xp, int *yp)
{
int t0 = *xp;
int t1 = *yp;
*xp = t1;
*yp = t0;
}
Body
Set
Up
Finish
swap:
pushl %ebp
movl %esp,%ebp
pushl %ebx
movl 8(%ebp), %edx
movl 12(%ebp), %ecx
movl (%edx), %ebx
movl (%ecx), %eax
movl %eax, (%edx)
movl %ebx, (%ecx)
popl %ebx
popl %ebp
ret

## Slide 54: Using Simple Addressing Modes
void swap(int *xp, int *yp)
{
int t0 = *xp;
int t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
pushl %ebp
movl %esp,%ebp
pushl %ebx
movl 8(%ebp), %edx
movl 12(%ebp), %ecx
movl (%edx), %ebx
movl (%ecx), %eax
movl %eax, (%edx)
movl %ebx, (%ecx)
popl %ebx
popl %ebp
ret
Body
Set
Up
Finish

## Slide 55: Understanding Swap
void swap(int *xp, int *yp)
{
int t0 = *xp;
int t1 = *yp;
*xp = t1;
*yp = t0;
}
Stack
(in memory)
Register Value
%edx xp
%ecx yp
%ebx t0
%eax t1
yp
xp
Rtn adr
Old %ebp
%ebp
0
4
8
12
Offset
•
•
•
Old %ebx
-4
%esp
movl 8(%ebp), %edx # edx = xp
movl 12(%ebp), %ecx # ecx = yp
movl (%edx), %ebx # ebx = *xp (t0)
movl (%ecx), %eax # eax = *yp (t1)
movl %eax, (%edx) # *xp = t1
movl %ebx, (%ecx) # *yp = t0

## Slide 56: Understanding Swap
0x120
0x124
Rtn adr
%ebp
0
4
8
12
Offset
-4
123
456
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
0x104
movl 8(%ebp), %edx # edx = xp
movl 12(%ebp), %ecx # ecx = yp
movl (%edx), %ebx # ebx = *xp (t0)
movl (%ecx), %eax # eax = *yp (t1)
movl %eax, (%edx) # *xp = t1
movl %ebx, (%ecx) # *yp = t0

## Slide 57: Understanding Swap
0x120
0x124
Rtn adr
%ebp
0
4
8
12
Offset
-4
123
456
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
0x124
0x104
0x120
movl 8(%ebp), %edx # edx = xp
movl 12(%ebp), %ecx # ecx = yp
movl (%edx), %ebx # ebx = *xp (t0)
movl (%ecx), %eax # eax = *yp (t1)
movl %eax, (%edx) # *xp = t1
movl %ebx, (%ecx) # *yp = t0

## Slide 58: Understanding Swap
0x120
0x124
Rtn adr
%ebp
0
4
8
12
Offset
-4
123
456
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
0x120
0x104
0x124
0x124
movl 8(%ebp), %edx # edx = xp
movl 12(%ebp), %ecx # ecx = yp
movl (%edx), %ebx # ebx = *xp (t0)
movl (%ecx), %eax # eax = *yp (t1)
movl %eax, (%edx) # *xp = t1
movl %ebx, (%ecx) # *yp = t0

## Slide 59: Understanding Swap
456
0x120
0x124
Rtn adr
%ebp
0
4
8
12
Offset
-4
123
456
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
0x124
0x120
123
0x104
movl 8(%ebp), %edx # edx = xp
movl 12(%ebp), %ecx # ecx = yp
movl (%edx), %ebx # ebx = *xp (t0)
movl (%ecx), %eax # eax = *yp (t1)
movl %eax, (%edx) # *xp = t1
movl %ebx, (%ecx) # *yp = t0

## Slide 60: Understanding Swap
0x120
0x124
Rtn adr
%ebp
0
4
8
12
Offset
-4
123
456
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
456
0x124
0x120
0x104
123
123
movl 8(%ebp), %edx # edx = xp
movl 12(%ebp), %ecx # ecx = yp
movl (%edx), %ebx # ebx = *xp (t0)
movl (%ecx), %eax # eax = *yp (t1)
movl %eax, (%edx) # *xp = t1
movl %ebx, (%ecx) # *yp = t0

## Slide 61: Understanding Swap
456
456
0x120
0x124
Rtn adr
%ebp
0
4
8
12
Offset
-4
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
456
456
0x124
0x120
123
0x104
123
movl 8(%ebp), %edx # edx = xp
movl 12(%ebp), %ecx # ecx = yp
movl (%edx), %ebx # ebx = *xp (t0)
movl (%ecx), %eax # eax = *yp (t1)
movl %eax, (%edx) # *xp = t1
movl %ebx, (%ecx) # *yp = t0

## Slide 62: Understanding Swap
0x120
0x124
Rtn adr
%ebp
0
4
8
12
Offset
-4
456
123
Address
0x124
0x120
0x11c
0x118
0x114
0x110
0x10c
0x108
0x104
0x100
yp
xp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
456
0x124
0x120
0x104
123
123
movl 8(%ebp), %edx # edx = xp
movl 12(%ebp), %ecx # ecx = yp
movl (%edx), %ebx # ebx = *xp (t0)
movl (%ecx), %eax # eax = *yp (t1)
movl %eax, (%edx) # *xp = t1
movl %ebx, (%ecx) # *yp = t0

## Slide 63: Homework
Review 3.1-3.3
Practice Problem 3.1

## Slide 64: Thank You