## Slide 1: Computer Organization Principles
School of Software, Dalian University of Technology
Chi Lin (林驰)
chilin@mail.dlut.edu.cn

## Slide 2: Chapter Five: Processor Architecture
Processor Organization (Architecture)
Processor Implementations (Realizations)
Instruction Pipeline (Optimizations)

## Slide 3: SEQ
Drawback:
  Low Throughput
  Waste of resources
  Big Latency
How to enhance the efficiency ?

## Slide 4: Instruction Pipeline
Computational Pipeline
Pipeline Hazards

## Slide 5: Computational Logic
Delay = Combinational logic delay + register delay
A signal controls the execution of the instruction.
A non-overlapping pipelined version is shown in Figure 4.32(b)

## Slide 6: Pipeline
A key feature of pipelining is that it increases the throughput of the system, that is, the number of customers served per unit time, but it may also slightly increase the latency, that is, the time required to service an individual customer.

## Slide 7: Divide one instruction into three stage execution model
The computation is divided into three stages, with the pipeline register latency 20ps

## Slide 8: Discuss
Advantages of pipeline
Disadvantages of pipeline
The more the better ?

## Slide 9: Clock triggered pipeline execution

## Slide 10: Two problems that diminish the performance of the pipeline
Non-uniform partition
Diminish returns of deep pipeline

## Slide 11: Time behavior of clock triggered pipeline

## Slide 12: Limitations of pipeline
An ideal pipeline
In reality...
Stages are uniformly divided.

## Slide 13: Diminishing returns of deep pipelines
The ratio between register latency and combination logic is big.

## Slide 14: Pipelined Y86 Implementations
PC update is shifted from the top.

## Slide 15: Pipelined Y86 Implementations PIPE-
Insert pipeline registers.
Fetch
Decode
Execute
Memory
Write back

## Slide 16: Y86 pipeline stages
F holds a predicted value of the program counter, as will be discussed shortly.
D sits between the fetch and decode stages. It holds information about the most recently fetched instruction for processing by the decode stage.
E sits between the decode and execute stages. It holds information about the most recently decoded instruction and the values read from the register file for processing by the execute stage.
M sits between the execute and memory stages. It holds the results of the most recently executed instruction for processing by the memory stage. It also holds information about branch conditions and branch targets for processing conditional jumps.
W sits between the memory stage and the feedback paths that supply the computed results to the register file for writing and the return address to the PC selection logic when completing a ret instruction.

## Slide 17: PIPE- drawbacks
Next PC Prediction-> jmp, call, ret
Pipeline hazards -> Data dependency & control dependency

## Slide 18: Pipeline Hazards
Data hazards: Data dependency
Control hazards: Control dependency

## Slide 19: Prog1: no hazards, no conflict

## Slide 20: Prog2: one nop omitted, hazard exists

## Slide 21: Prog3: two nops omitted, hazards exist

## Slide 22: Hazard 4

## Slide 23: Prog4: no nops, multiple hazards

## Slide 24: Classes of data hazards
Program registers: These are the hazards we have already identified. They arise because the register file is read in one stage and written in another, leading to possible unintended interactions between different instructions.

## Slide 25: Classes of data hazards
Program counter: Conflicts between updating and reading the program counter give rise to control hazards. No hazard arises when our fetch-stage logic correctly predicts the new value of the program counter before fetching the next instruction. Mispredicted branches and ret instructions require special handling.

## Slide 26: Classes of data hazards
Memory: Writes and reads of the data memory both occur in the memory stage. By the time an instruction reading memory reaches this stage, any preceding instructions writing memory will have already done so. On the other hand, there can be interference between instructions writing data in the memory stage and the reading of instructions in the fetch stage, since the instruction and data memories reference a single address space. This can only happen with programs containing self-modifying code, where instructions write to a portion of memory from which instructions are later fetched. Some systems have complex mechanisms to detect and avoid such hazards, while others simply mandate that programs should not use self modifying code. We will assume for simplicity that programs do not modify themselves, and therefore we do not need to take special measures to update the instruction memory based on updates to the data memory during program execution.

## Slide 27: Classes of data hazards
Condition code register: These are written by integer operations in the execute stage. They are read by conditional moves in the execute stage and by conditional jumps in the memory stage. By the time a conditional move or jump reaches the execute stage, any preceding integer operation will have already completed this stage. No hazards can arise.

## Slide 28: Classes of data hazards
Status register: The program status can be affected by instructions as they flow through the pipeline. Our mechanism of associating a status code with each instruction in the pipeline enables the processor to come to an orderly halt when an exception occurs,

## Slide 29: Hazards Avoiding (Stalling)
One very general technique for avoiding hazards involves stalling, where the processor holds back one or more instructions in the pipeline until the hazard condition no longer holds.

## Slide 30: Hazards Avoiding (Stalling)
prog4: 3 bubble inserted

## Slide 31: Stalling Drawbacks
Wait….
Wait….
Wait….
Let’s discuss how to solve it.

## Slide 32: Forwarding
Rather than stalling until the write has completed, it can simply pass the value that is about to be written to pipeline register E as the source operand.

## Slide 33: Hazards Avoiding (Forwarding)

## Slide 34: Hazards Avoiding (Forwarding)

## Slide 35: Hazards Avoiding (Forwarding)

## Slide 36: Forwarding Drawbacks
Additional signals
Additional registers for save temporary information.

## Slide 37: Final version PIPE

## Slide 38: Pipeline vs PC
Discuss the relationships between pipeline and PC.

## Slide 39: Wow, amazing
Fetch
Decode
Execute
PC
(PC)-1
(PC)-2
Why do you use (PC)-1 rather than PC-1

## Slide 40: Ideal Pipeline
周期
操作
addl
subl
andl
irmovl
xorl
rrmovl
1
2
3
4
5
6
7
8
9
F
D
E
W
F
D
E
W
F
E
W
F
D
E
W
F
D
W
E
F
D
E
W
F – 取指（Fetch）D – 解码（Decode） E – 执行（Execute）
M – 存储器（Memory ）W –写回（ Writeback）
M
D
One Critical Preliminary:
No data or control dependency

## Slide 41: In reality, another pipeline hazards may occur

## Slide 42: However, some instructions will cause the pipeline hazards
Try to think which kind of instruction will cause this result.
jXX
ret
call ?

## Slide 43: A deep insight to pipeline hazard
So, we can conclude that the call instruction will not cause the pipeline hazard

## Slide 44: Braches Effect (the ret instruction)
When the W stage is over, the F instruction is taken.

## Slide 45: How to further enhance the performance ?
Fetch prediction (4.5.11)
PC selection (4.5.10)
Your powerful imagination.

## Slide 46: Chapter Summary
How to design a processor?
  ISA: visible state, encodings
  Program execution: Fetch, Decode, Execute, Memory, Write
  Pipeline: Design, hazards

## Slide 47: Homework
Practice Problem 4.27
Review Chapter 4.1 4.3 4.4 4.5 4.6

## Slide 48: Mission Complete!
Information Representation
Instruction
Processor
Memory Easy
I/O Easy
Control Unit Easy
Mom will no longer worry about my study.

## Slide 49: Thank You