## Slide 1: Computer Organization Principles
School of Software, Dalian University of Technology
Chi Lin (林驰)
chilin@mail.dlut.edu.cn

## Slide 2: Great Reality #4: Memory Matters Random Access Memory Is an Unphysical Abstraction
Carnegie Mellon
Memory is not unbounded
  It must be allocated and managed
  Many applications are memory dominated
Memory referencing bugs especially pernicious(致命的)
  Effects are distant in both time and space
Memory performance is not uniform
  Cache and virtual memory effects can greatly affect program performance
  Adapting program to characteristics of memory system can lead to major speed improvements

## Slide 3: Memory System Performance Example
Carnegie Mellon
Hierarchical memory organization
Performance depends on access patterns
  Including how step through multi-dimensional array
void copyji(int src[2048][2048],
int dst[2048][2048])
{
int i,j;
for (j = 0; j < 2048; j++)
for (i = 0; i < 2048; i++)
dst[i][j] = src[i][j];
}
void copyij(int src[2048][2048],
int dst[2048][2048])
{
int i,j;
for (i = 0; i < 2048; i++)
for (j = 0; j < 2048; j++)
dst[i][j] = src[i][j];
}
21 times slower (Pentium 4)

## Slide 4: The Memory Mountain
Carnegie Mellon
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12 | s13 | s14 | s15 | s16 | s32 | s64
64M | 4029.59 | 2752.75 | 2159.29 | 1710.75 | 1391.48 | 1176.29 | 1015.77 | 890.72 | 845.57 | 805.46 | 773.78 | 757.94 | 727.91 | 712.66 | 705.63 | 701.98 | 598.19 | 601.22
32M | 4029.36 | 2752.39 | 2160.62 | 1710.98 | 1391.5 | 1176.54 | 1016.71 | 891.8 | 846.98 | 807.22 | 775.18 | 760.41 | 730.74 | 714.98 | 709.26 | 708.88 | 608.99 | 607.39
16M | 4040.1 | 2788.42 | 2188.92 | 1742.97 | 1421.69 | 1201.31 | 1038.37 | 911.7 | 870.39 | 835.31 | 809.25 | 798.05 | 780.28 | 778.37 | 787.2 | 744.13 | 633.53 | 608.86
8M | 4374.01 | 3610.74 | 3002.03 | 2492.39 | 2131.04 | 1821.71 | 1564.14 | 1414.18 | 1404.78 | 1408.59 | 1423.67 | 1456.86 | 1499.61 | 1600.13 | 1667.47 | 1231.7 | 1078.97 | 1026.03
4M | 4642.47 | 4583.8 | 4074.93 | 3557.51 | 3337.59 | 2898.78 | 2535.22 | 2248.83 | 2227.41 | 2203.98 | 2187.29 | 2164.18 | 2156.96 | 2148.52 | 2146.83 | 2131.36 | 2038.29 | 2060.87
2M | 4674.06 | 4659.06 | 4153.1 | 4016.4 | 3540.78 | 3027.05 | 2625.06 | 2321.73 | 2306.4 | 2292.86 | 2282.38 | 2270.35 | 2264.14 | 2259.8 | 2260.46 | 2261.54 | 2224.92 | 2431.58
1M | 4673.77 | 4656.98 | 4156.32 | 4012.65 | 3535.85 | 3021.82 | 2623.08 | 2318.19 | 2303.72 | 2291.55 | 2280.42 | 2270.24 | 2264.82 | 2261.86 | 2261.31 | 2271.41 | 2237.27 | 2432.74
512K | 4673 | 4658.05 | 4267.3 | 4052.55 | 3730.88 | 3236.67 | 2839.93 | 2527.15 | 2513.25 | 2503.12 | 2494.19 | 2517.44 | 2523.1 | 2551.67 | 2555.53 | 2477.41 | 2420.17 | 2590.64
256K | 4672.31 | 4645.58 | 4300.1 | 4091.3 | 3890.2 | 3175.38 | 2748.26 | 2351.27 | 2518.38 | 2627.49 | 2644.71 | 2646.45 | 2690.79 | 2715.46 | 2762.7 | 2445.48 | 2440.11 | 2560.87
128K | 4669.89 | 4661.44 | 4661.75 | 4570.55 | 4453.42 | 4070.1 | 3626.17 | 2349.05 | 3332.47 | 3318.78 | 3328.21 | 3312.1 | 3351.75 | 3197.56 | 3342.59 | 3330.51 | 3335.4 | 3374.9
64K | 4664.69 | 4647.96 | 4646.51 | 4575.1 | 4473.68 | 4218.51 | 3642.61 | 3334.78 | 3395.82 | 3398 | 3403.08 | 3411.87 | 3395.99 | 3299.01 | 4287.45 | 3416.74 | 3389.13 | 3374.16
32K | 4654.62 | 4624.5 | 4631.69 | 4615.62 | 4600.39 | 4585.6 | 4572.8 | 4809.1 | 4803.13 | 4789.7 | 4790.97 | 4784.65 | 4754.23 | 4768.54 | 4750.25 | 4742.01 | 6545.16 | 6408.41
Intel Core i7
2.67 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache

## Slide 5: Chapter Six：Memory
6.1 Memory Hierarchy
6.2 Cache
6.3 Virtual Memory

## Slide 6: 6.1 Memory Hierarchy
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy

## Slide 7: 6.1 Memory Hierarchy
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy

## Slide 8: Developing Trends

## Slide 9: Summary of Memory
Memory dominated applications.
  Speed
  DMA
  Information Exchange

## Slide 10: Memory Category
Physical Type
  Semiconductor：TTL、MOS
  small, low cost, fast, volatile
  Magnetic: disk(磁盘), tape(磁带), magnetic drum(磁鼓)
  Optical: CD, CD-R, CD-RW, DVD, Blue-ray DVD
volatile
Non-
volatile

## Slide 11: Storage Type
Random Access Memory
  Volatile
  SRAM(Cache), DRAM(内存)
Read Only Memory
  Non-volatile
  掩膜型只读存储器（ROM）、可编程只读存储器（PROM）、可擦除可编程只读存储器（EPROM）、电可擦除可编程只读存储器（EEPROM）、闪速存储器（Flash Memory）
Notes: ROM指的是“只读存储器”，即Read-Only Memory。这是一种线路最简单半导体电路，通过掩模工艺， 一次性制造，其中的代码与数据将永久保存(除非坏掉)，不能进行修改。这玩意一般在大批量生产时才会被用的，优点是成本低、非常低，但是其风险比较大，在产品设计时，如果调试不彻底，很容易造成几千片的费片，行内话叫“掩砸了”！ PROM指的是“可编程只读存储器”既Programmable Red-Only Memory。这样的产品只允许写入一次，所以也被称为“一次可编程只读存储器”(One Time Progarmming ROM，OTP-ROM)。PROM在出厂时，存储的内容全为1，用户可以根据需要将其中的某些单元写入数据0(部分的PROM在出厂时数据全为0，则用户可以将其中的部分单元写入1)， 以实现对其“编程”的目的。PROM的典型产品是“双极性熔丝结构”，如果我们想改写某些单元，则可以给这些单元通以足够大的电流，并维持一定的时间，原先的熔丝即可熔断，这样就达到了改写某些位的效果。另外一类经典的PROM为使用“肖特基二极管”的PROM，出厂时，其中的二极管处于反向截止状态，还是用大电流的方法将反相电压加在“肖特基二极管”，造成其永久性击穿即可。 EPROM指的是“可擦写可编程只读存储器”，即Erasable Programmable Read-Only Memory。 它的特点是具有可擦除功能，擦除后即可进行再编程，但是缺点是擦除需要使用紫外线照射一定的时间。这一类芯片特别容易识别，其封装中包含有“石英玻璃窗”，一个编程后的EPROM芯片的“石英玻璃窗”一般使用黑色不干胶纸盖住， 以防止遭到阳光直射。 EEPROM指的是“电可擦除可编程只读存储器”，即Electrically Erasable Programmable Read-Only Memory。它的最大优点是可直接用电信号擦除，也可用电信号写入。EEPROM不能取代RAM的原应是其工艺复杂， 耗费的门电路过多，且重编程时间比较长，同时其有效重编程次数也比较低。 Flash memory指的是“闪存”，所谓“闪存”，它也是一种非易失性的内存，属于EEPROM的改进产品。它的最大特点是必须按块(Block)擦除(每个区块的大小不定，不同厂家的产品有不同的规格)， 而EEPROM则可以一次只擦除一个字节(Byte)。目前“闪存”被广泛用在PC机的主板上，用来保存BIOS程序，便于进行程序的升级。其另外一大应用领域是用来作为硬盘的替代品，具有抗震、速度快、无噪声、耗电低的优点，但是将其用来取代RAM就显得不合适，因为RAM需要能够按字节改写，而Flash ROM做不到。

## Slide 12: ROM
Read-only memory (ROM) is a class of storage medium used in computers and other electronic devices.
Strictly, read-only memory refers to memory that is hard-wired, such as diode matrix and the later mask ROM.
The fact that such memory can never be changed is a large drawback; more recently, ROM commonly refers to memory that is read-only in normal operation.

## Slide 13: PROM
A programmable read-only memory (PROM) is a form of digital memory where the setting of each bit is locked by a fuse or antifuse.
They are a type of ROM (read-only memory) meaning the data in them is permanent and cannot be changed. PROMs are used in digital electronic devices to store permanent data, usually low level programs such as firmware (microcode).
The key difference from a standard ROM is that the data is written into a ROM during manufacture, while with a PROM the data is programmed into them after manufacture.
Notes: 1.一次编程只读存储器（ROM） 可编程只读存储器只允许写入一次，所以也被称为“一次可编程只读存储器”(One Time Progarmming ROM，OTP-ROM)。PROM在出厂时，存储的内容全为1，用户可以根据需要将其中的某些单元写入数据0(部分的PROM在出厂时数据全为0，则用户可以将其中的部分单元写入1)， 以实现对其“编程”的目的。PROM的典型产品是“双极性熔丝结构”，如果我们想改写某些单元，则可以给这些单元通以足够大的电流，并维持一定的时间，原先的熔丝即可熔断，这样就达到了改写某些位的效果。另外一类经典的PROM为使用“肖特基二极管”的PROM，出厂时，其中的二极管处于反向截止状态，还是用大电流的方法将反相电压加在“肖特基二极管”，造成其永久性击穿即可。

## Slide 14: EPROM
Once programmed, an EPROM can be erased by exposing it to strong ultraviolet light source (such as from a mercury-vapor light)
紫外线接收窗

## Slide 15: EEPROM
EEPROM stands for Electrically Erasable Programmable Read-Only Memory and is a type of non-volatile memory used in computers and other electronic devices to store small amounts of data that must be saved when power is removed.

## Slide 16: FLASH

## Slide 17: FLASH vs EEPROM, RAM
FLASH vs EEPROM
  Fast Reading & Writing
  Large Capacity
FLASH vs RAM
  Non-volitile

## Slide 18: Summary of Memory
Disk, CD, DVD…
Cache
Flash Memory
Memory
Main Memory
External Memory
MROM
PROM
EPROM
EEPROM
RAM
ROM
DRAM
SRAM

## Slide 19: Random-Access Memory (RAM)
Key features
  RAM is traditionally packaged as a chip.
  Basic storage unit is normally a cell (one bit per cell).
  Multiple RAM chips form a memory.
Static RAM (SRAM)
  Each cell stores a bit with a four or six-transistor circuit (6晶体管电路
  Retains value indefinitely, as long as it is kept powered.
  Relatively insensitive to electrical noise (EMI), radiation, etc.
  Faster and more expensive than DRAM.

## Slide 20: Random Access Memory(RAM)
Dynamic RAM (DRAM)
  Each cell stores bit with a capacitor(电容). One transistor(晶体管) is used for access
  Value must be refreshed(更新、充电) every 10-100 ms.
  More sensitive to disturbances (EMI, radiation,…) than SRAM.
  Slower and cheaper than SRAM.

## Slide 21: SRAM vs DRAM Summary
Trans. Access Needs Needs
per bit time refresh? EDC? Cost Applications
SRAM 4 or 6 1X No Maybe 100x Cache memories
DRAM 1 10X Yes Yes 1X Main memories,
frame buffers

## Slide 22: Key Characteristic of Main Memory
Memory Capacity: Number of binary bit in memory
  Capacity=Number of storage unit×word

## Slide 23: Conventional DRAM Organization
d * w DRAM:
  dw total bits organized as d supercells of size w bits
cols
rows
0
1
2
3
0
1
2
3
Internal row buffer
16 x 8 DRAM chip
addr
data
supercell
(2,1)
2 bits
/
8 bits
/
Memory
controller
(to/from CPU)

## Slide 24: Reading DRAM Supercell (2,1)
Step 1(a): Row access strobe (RAS) selects row 2.
Step 1(b): Row 2 copied from DRAM array to row buffer.
Cols
Rows
RAS = 2
0
1
2
3
0
1
2
Internal row buffer
16 x 8 DRAM chip
3
addr
data
2
/
8
/
Memory
controller

## Slide 25: Reading DRAM Supercell (2,1)
Step 2(a): Column access strobe (CAS) selects column 1.
Step 2(b): Supercell (2,1) copied from buffer to data lines, and eventually back to the CPU.
Cols
Rows
0
1
2
3
0
1
2
3
Internal row buffer
16 x 8 DRAM chip
CAS = 1
addr
data
2
/
8
/
Memory
controller
supercell
(2,1)
supercell
(2,1)
To CPU

## Slide 26: Memory Modules
: supercell (i,j)
64 MB
memory module
consisting of
eight 8Mx8 DRAMs
addr (row = i, col = j)
Memory
controller
DRAM 7
DRAM 0
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56
64-bit doubleword at main memory address A
bits
0-7
bits
8-15
bits
16-23
bits
24-31
bits
32-39
bits
40-47
bits
48-55
bits
56-63
64-bit doubleword
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56

## Slide 27: Enhanced DRAMs
Basic DRAM cell has not changed since its invention in 1966.
  Commercialized by Intel in 1970.
DRAM cores with better interface logic and faster I/O :
  Synchronous DRAM (SDRAM)
    Uses a conventional clock signal instead of asynchronous control
    Allows reuse of the row addresses (e.g., RAS, CAS, CAS, CAS)

## Slide 28: SDRAM

## Slide 29: Chip Select（BA0，BA1）

## Slide 30: SDRAM

## Slide 31: Enhanced DRAMs
  Double data-rate synchronous DRAM (DDR SDRAM)
    Double edge clocking (双沿时钟) sends two bits per cycle per pin
    Different types distinguished by size of small prefetch buffer:
      DDR (2 bits), DDR2 (4 bits), DDR4 (8 bits)
    By 2010, standard for most server and desktop systems
    Intel Core i7 supports only DDR3 SDRAM

## Slide 32: Nonvolatile Memories
DRAM and SRAM are volatile memories
  Lose information if powered off.
Nonvolatile memories retain value even if powered off
  Read-only memory (ROM): programmed during production
  Programmable ROM (PROM): can be programmed once
  Eraseable PROM (EPROM): can be bulk erased (UV, X-Ray)
  Electrically eraseable PROM (EEPROM): electronic erase capability
  Flash memory: EEPROMs with partial (sector) erase capability
    Wears out after about 100,000 erasings.

## Slide 33: Nonvolatile Memories
Uses for Nonvolatile Memories
  Firmware programs stored in a ROM (BIOS, controllers for disks, network cards, graphics accelerators, security subsystems,…)
  Solid state disks (replace rotating disks in thumb drives, smart phones, mp3 players, tablets, laptops,…)
  Disk caches

## Slide 34: Traditional Bus Structure Connecting CPU and Memory
A bus is a collection of parallel wires that carry address, data, and control signals.
Buses are typically shared by multiple devices.
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus

## Slide 35: Memory Read Transaction (1)
CPU places address A on the memory bus.
ALU
Register file
Bus interface
A
0
A
x
Main memory
I/O bridge
%eax
Load operation: movl A, %eax

## Slide 36: Memory Read Transaction (2)
Main memory reads A from the memory bus, retrieves word x, and places it on the bus.
ALU
Register file
Bus interface
x
0
A
x
Main memory
%eax
I/O bridge
Load operation: movl A, %eax

## Slide 37: Memory Read Transaction (3)
CPU read word x from the bus and copies it into register %eax.
x
ALU
Register file
Bus interface
x
Main memory
0
A
%eax
I/O bridge
Load operation: movl A, %eax

## Slide 38: Memory Write Transaction (1)
CPU places address A on bus. Main memory reads it and waits for the corresponding data word to arrive.
y
ALU
Register file
Bus interface
A
Main memory
0
A
%eax
I/O bridge
Store operation: movl %eax, A

## Slide 39: Memory Write Transaction (2)
CPU places data word y on the bus.
y
ALU
Register file
Bus interface
y
Main memory
0
A
%eax
I/O bridge
Store operation: movl %eax, A

## Slide 40: Memory Write Transaction (3)
Main memory reads data word y from the bus and stores it at address A.
y
ALU
register file
bus interface
y
main memory
0
A
%eax
I/O bridge
Store operation: movl %eax, A

## Slide 41: Memory Read Transaction
MAR
MDR
CPU
主存存储器
AB
DB
CB
Read
ready
Read
主存存储器
CPU
主存存储器
Notes: 存储器用来暂时存储CPU正在使用的指令和数据，它和CPU的关系最为密切。主存储器和CPU的连接是由总线支持的，连接形式如图4.1所示。总线包括数据总线、地址总线和控制总线。CPU通过使用AR(地址寄存器)和DR(数码寄存器)和主存进行数据传送。若AR为K位字长，DR为n位字长，则允许主存包含2K个可寻址单位(字节或字)。在一个存储周期内，CPU和主存之间通过总线进行n位数据传送。此外，控制总线包括控制数据传送的读(read)、写(write)和表示存储器功能完成的(ready)控制线。
为了从存储器中取一个信息字，CPU必须指定存储器字地址，并进行“读”操作。CPU需要把信息字的地址送到AR，经地址总线送往主存储器。同时，CPU应用控制线(read)发一个“读”请求。此后，CPU等待从主存储器发来的回答信号，通知CPU“读”操作完成。主存储器通过ready线做出回答，若ready信号为“1”，说明存储字的内容已经读出，并放在数据总线上，送入DR。这时，“取”数操作完成。

## Slide 42: Memory Write Transaction
MAR
MDR
CPU
主存存储器
AB
DB
CB
Write
ready
Write
CPU
主存存储器
主存存储器
CPU
Notes: 为了“存”一个字到主存，CPU先将信息字在主存中的地址经AR送地址总线，并将信息字送DR。同时，发出“写”命令。此后，CPU等待写操作完成信号。主存储器从数据总线接收到信息字并按地址总线指定的地址存储，然后经ready控制线发回存储器操作完成信号。这时，“存”数操作完成。
从以上讨论可见，CPU与主存之间采取异步工作方式，以ready信号表示一次访存操作的结束。

## Slide 43: Main Memory Address
24 address lines
Byte addressing
Word addressing
Word: 16 bit
Word addressing
Word: 32 bit
Word address
Byte Address
11
10
9
8
7
6
5
4
3
2
1
0
8
4
0
224 = 16 M
8 M
4 M
Usually, addressing unit are word and byte

## Slide 44: Big Endian vs Small Endian
MSB  Low Address Big
MSB High Address Small
21
43
65
87
22H
23H
24H
25H
26H
27H
28H
24H
0x87654321

## Slide 45: Connection between Memory & CPU
Memory Extension
  Bit extension (位扩展)
  Word extension (字扩展)
  Bit & word extension (字位同时扩展)
Connection between memory and CPU
  Data lines, address lines, chip select lines (CS), read-write control

## Slide 46: bit extension
1K × 4bit -> 1K × 8bit
D
D
…
…
D
0
4
7
9
A
A
0
•••
2114
2114
CS
WE

## Slide 47: Word Extension
1K × 8bit -> 2K × 8位
1K× 8位
1K× 8位
D7
D0
•••
•••
•••
•••
•••
WE
A1
A0
•••
A9
CS0
A10
1
CS1

## Slide 48: 3、Bit & Word Extension
1K × 4bit -> 4K × 8bit
WE
A8
A9
A0
...
D7
D0
…
A11
A10
CS0
CS1
CS2
CS3
片选
译码
…
…
…
…
…
…
…
…
1K×4
1K×4
1K×4
1K×4
1K×4
1K×4
1K×4
1K×4

## Slide 49: What’s Inside A Disk Drive?
Spindle
Arm
Actuator
Platters
Electronics
(including a
processor
and memory!)
SCSI
connector
Image courtesy of Seagate Technology

## Slide 50: Disk Geometry
Disks consist of platters(盘片), each with two surfaces盘面.
Each surface consists of concentric rings called tracks磁道.
Each track consists of sectors扇区 separated by gaps.
Spindle
Surface
Tracks
Track k
Sectors
Gaps

## Slide 51: Disk Geometry (Muliple-Platter View)
Aligned tracks form a cylinder.
Surface 0
Surface 1
Surface 2
Surface 3
Surface 4
Surface 5
Cylinder k
Spindle
Platter 0
Platter 1
Platter 2

## Slide 52: Disk Capacity
Capacity: maximum number of bits that can be stored.
Capacity is determined by these technology factors:
  Recording density (bits/in): number of bits that can be squeezed into a 1 inch segment of a track.
  Track density (tracks/in): number of tracks that can be squeezed into a 1 inch radial segment.
  Areal density (bits/in2): product of recording and track density.

## Slide 53: Disk Capacity
Modern disks partition tracks into disjoint subsets called recording zones
  Each track in a zone has the same number of sectors(每个磁道的扇区数量相同), determined by the circumference of innermost track(由最内侧周长决定).
  Each zone has a different number of sectors/track

## Slide 54: Computing Disk Capacity
Capacity = (# bytes/sector) x (avg. # sectors/track) x
(# tracks/surface) x (# surfaces/platter) x
(# platters/disk)
Example:
  512 bytes/sector
  300 sectors/track (on average)
  20,000 tracks/surface
  2 surfaces/platter
  5 platters/disk
Capacity = 512 x 300 x 20000 x 2 x 5
= 30,720,000,000
= 30.72 GB

## Slide 55: Disk Operation (Single-Platter View)
The disk surface
spins at a fixed
rotational rate
By moving radially, the arm can position the read/write head over any track.
The read/write head
is attached to the end
of the arm and flies over
the disk surface on
a thin cushion of air.
spindle
spindle
spindle
spindle
spindle

## Slide 56: Disk Operation (Multi-Platter View)
Arm
Read/write heads
move in unison
from cylinder to cylinder
Spindle（主轴）

## Slide 57: Disk Structure - top view of single platter
Tracks divided into sectors
Surface organized into tracks
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 58: Disk Access
Head in position above a track
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 59: Disk Access
Rotation is counter-clockwise
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 60: Disk Access – Read
About to read blue sector
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 61: Disk Access – Read
After BLUE read
After reading blue sector
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 62: Disk Access – Read
After BLUE read
Red request scheduled next
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 63: Disk Access – Seek
After BLUE read
Seek for RED
Seek to red’s track
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 64: Disk Access – Rotational Latency
After BLUE read
Seek for RED
Rotational latency
Wait for red sector to rotate around
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 65: Disk Access – Read
After BLUE read
Seek for RED
Rotational latency
After RED read
Complete read of red
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 66: Disk Access – Service Time Components
After BLUE read
Seek for RED
Rotational latency
After RED read
Data transfer
Seek
Rotational
latency
Data transfer
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 67: Disk Access Time
Disks read and write data in sector-sized blocks.
The access time for a sector has three main components: seek time, rotational latency and transfer time
Average time to access some target sector approximated by :
  Taccess = Tavg seek + Tavg rotation + Tavg transfer

## Slide 68: Disk Access Time
Seek time (Tavg seek)
  Time to position heads over cylinder containing target sector.
  Typical Tavg seek is 3—9 ms
Rotational latency (Tavg rotation)
  Time waiting for first bit of target sector to pass under r/w head.
  Tavg rotation = 1/2 x 1/RPMs(Revolutions Perminute转/每分钟 ) x 60 sec/1 min
  Typical Tavg rotation = 7200 RPMs
Transfer time (Tavg transfer)
  Time to read the bits in the target sector.
  Tavg transfer = 1/RPM x 1/(avg # sectors/track) x 60 secs/1 min.

## Slide 69: Disk Access Time Example
Given:
  Rotational rate = 7,200 RPM
  Average seek time = 9 ms.
  Avg # sectors/track = 400.
Derived:
  Tavg rotation = 1/2 x (60 secs/7200 RPM) x 1000 ms/sec = 4 ms.
  Tavg transfer = 60/7200 RPM x 1/400 secs/track x 1000 ms/sec = 0.02 ms
  Taccess = 9 ms + 4 ms + 0.02 ms

## Slide 70: Disk Access Time Example
Important points:
  Access time dominated by seek time and rotational latency.
  First bit in a sector is the most expensive, the rest are free.
  SRAM access time is about 4 ns/doubleword, DRAM about 60 ns
    Disk is about 40,000 times slower than SRAM,
    2,500 times slower then DRAM.

## Slide 71: Logical Disk Blocks
Modern disks present a simpler abstract view of the complex sector geometry:
  The set of available sectors is modeled as a sequence of b-sized logical blocks (0, 1, 2, ...)
Mapping between logical blocks and actual (physical) sectors
  Maintained by hardware/firmware device called disk controller.
  Converts requests for logical blocks into (surface,track,sector) triples.

## Slide 72: I/O Bus
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Expansion slots for
other devices such
as network adapters.

## Slide 73: Reading a Disk Sector (1)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
mouse
keyboard
Monitor
Disk
I/O bus
Bus interface
CPU initiates a disk read by writing a command, logical block number, and destination memory address to a port (address) associated with disk controller.

## Slide 74: Reading a Disk Sector (2)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Bus interface
Disk controller reads the sector and performs a direct memory access (DMA) transfer into main memory.

## Slide 75: Reading a Disk Sector (3)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Bus interface
When the DMA transfer completes, the disk controller notifies the CPU with an interrupt (i.e., asserts a special “interrupt” pin on the CPU)

## Slide 76: Solid State Disk (SSD)
Flash Memory
No rotating equipment
Faster than Disks

## Slide 77: Solid State Disks (SSDs)
Pages: 512KB to 4KB, Blocks: 32 to 128 pages
Data read/written in units of pages.
Page can be written only after its block has been erased
A block wears out after 100,000 repeated writes.
Flash
translation layer
I/O bus
Page 0
Page 1
Page P-1
…
Block 0
…
Page 0
Page 1
Page P-1
…
Block B-1
Flash memory
Solid State Disk (SSD)
Requests to read and
write logical disk blocks

## Slide 78: SSD Performance Characteristics
Why are random writes so slow?
  Erasing a block is slow (around 1 ms)
  Write to a page triggers a copy of all useful pages in the block
    Find an used block (new block) and erase it
    Write the page into the new block
    Copy other pages from old block to the new block
Sequential read tput 250 MB/s Sequential write tput 170 MB/s
Random read tput 140 MB/s Random write tput 14 MB/s
Rand read access 30 us Random write access 300 us

## Slide 79: SSD Tradeoffs vs Rotating Disks
Advantages
  No moving parts  faster, less power, more rugged
Disadvantages
  Have the potential to wear out
    Mitigated by “wear leveling logic” in flash translation layer(寿命影响)
    E.g. Intel X25 guarantees 1 petabyte (1015 bytes) of random writes before they wear out
  In 2010, about 100 times more expensive per byte
Applications
  MP3 players, smart phones, laptops
  Beginning to appear in desktops and servers

## Slide 80: Storage Trends

## Slide 81: CPU Clock Rates
1980 1990 1995 2000 2003 2005 2010 2010:1980
CPU 8080 386 Pentium P-III P-4 Core 2 Core i7 ---
Clock
rate (MHz) 1 20 150 600 3300 2000 2500 2500
Cycle
time (ns) 1000 50 6 1.6 0.3 0.50 0.4 2500
Cores 1 1 1 1 1 2 4 4
Effective
cycle 1000 50 6 1.6 0.3 0.25 0.1 10,000
time (ns)
Inflection point in computer history
when designers hit the “Power Wall”

## Slide 82: The CPU-Memory Gap
The gap widens between DRAM, disk, and CPU speeds.
Chart: Year
| 1980 | 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010
Disk seek time | 87000000 | 75000000 | 28000000 | 10000000 | 8000000 | 8000000 | 8000000 | 8000000
Flash SSD access time | 75000
DRAM access time | 375 | 200 | 100 | 70 | 60 | 55 | 50 | 40
SRAM access time | 300 | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5
CPU cycle time | 1000 | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4
Effective CPU cycle time | 0.3 | 0.25 | 0.1
Disk
DRAM
CPU
SSD

## Slide 83: Locality to the Rescue!
The key to bridging this CPU-Memory gap is a fundamental property of computer programs known as locality.

## Slide 84: Homework
Practice Problem 6.1-6.4
Review Chapter 6.1

## Slide 85: Today
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy

## Slide 86: Locality
Principle of Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 87: Locality Example
Data references
  Reference array elements in succession (连续) (stride-1 reference pattern).
  Reference variable sum each iteration.
Instruction references
  Reference instructions in sequence.
  Cycle through loop repeatedly.
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial locality
Temporal locality
Spatial locality
Temporal locality

## Slide 88: Qualitative Estimates of Locality
Claim: Being able to look at code and get a qualitative sense of its locality is a key skill for a professional programmer.
Question: Does this function have good locality with respect to array a?
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}

## Slide 89: Locality Example
Question: Does this function have good locality with respect to array a?
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}

## Slide 90: Locality Example
Question: Can you permute the loops so that the function scans the 3-d array a with a stride-1 reference pattern (and thus has good spatial locality)?
int sum_array_3d(int a[M][N][N])
{
int i, j, k, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
for (k = 0; k < N; k++)
sum += a[k][i][j];
return sum;
}

## Slide 91: Memory Hierarchies
Some fundamental and enduring properties of hardware and software:
  Fast storage technologies cost more per byte, have less capacity, and require more power (heat!).
  The gap between CPU and main memory speed is widening.
  Well-written programs tend to exhibit good locality.
These fundamental properties complement each other beautifully.
They suggest an approach for organizing memory and storage systems known as a memory hierarchy.

## Slide 92: Today
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy

## Slide 93: Storage Structure in Computer
低
CPU
Memory
Disk
CD
CU
ALU
Register
cache

## Slide 94: An Example Memory Hierarchy
Registers
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
cheaper
per byte
Remote secondary storage
(tapes, distributed file systems, Web servers)
Local disks hold files retrieved from disks on remote network servers
Main memory holds disk blocks retrieved from local disks
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from L2 cache
CPU registers hold words retrieved from L1 cache
L2 cache holds cache lines retrieved from main memory
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
costlier
per byte

## Slide 95
Two layers
Cache——Memory
Speed, Cost gap
Memory——External Memory
Speed, Capacity, Cost
Cache
CPU
Memory
External Memory
10 ns
20 ns
200 ns
ms

## Slide 96: Caches
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device.
Fundamental idea of a memory hierarchy:
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1.
Why do memory hierarchies work?
  Because of locality, programs tend to access the data at level k more often than they access the data at level k+1.
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit.

## Slide 97: Caches
Big Idea: The memory hierarchy creates a large pool of storage that costs as much as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top.

## Slide 98: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10

## Slide 99: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!

## Slide 100: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)

## Slide 101: General Caching Concepts: Types of Cache Misses
Cold (compulsory) miss
  Cold misses occur because the cache is empty.
Conflict miss
  Most caches limit blocks at level k+1 to a small subset (sometimes a singleton) of the block positions at level k.
    E.g. Block i at level k+1 must be placed in block (i mod 4) at level k.
  Conflict misses occur when the level k cache is large enough, but multiple data objects all map to the same level k block.
    E.g. Referencing blocks 0, 8, 0, 8, 0, 8, ... would miss every time.
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache.

## Slide 102: Examples of Caching in the Hierarchy
Hardware
0
On-Chip TLB
Address translations
TLB
Web browser
10,000,000
Local disk
Web pages
Browser cache
Web cache
Network buffer cache
Buffer cache
Virtual Memory
L2 cache
L1 cache
Registers
Cache Type
Web pages
Parts of files
Parts of files
4-KB page
64-bytes block
64-bytes block
4-8 bytes words
What is Cached?
Web proxy server
1,000,000,000
Remote server disks
OS
100
Main memory
Hardware
1
On-Chip L1
Hardware
10
On/Off-Chip L2
AFS/NFS client
10,000,000
Local disk
Hardware + OS
100
Main memory
Compiler
0
CPU core
Managed By
Latency (cycles)
Where is it Cached?
Disk cache
Disk sectors
Disk controller
100,000
Disk firmware

## Slide 103: Summary
The speed gap between CPU, memory and mass storage continues to widen.
Well-written programs exhibit a property called locality.
Memory hierarchies based on caching close the gap by exploiting locality.

## Slide 104: 6.2 Cache
Cache memory organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 105: Cache Memories
Cache memories are small, fast SRAM-based memories managed automatically in hardware.
  Hold frequently accessed blocks of main memory
CPU looks first for data in caches (e.g., L1, L2, and L3), then in main memory.
Typical system structure:
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Cache
memories

## Slide 106: General Cache Organization (S, E, B)
E = 2e lines per set
S = 2s sets
set
line
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size:
C = S x E x B data bytes
valid bit

## Slide 107: Cache Read
E = 2e lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset

## Slide 108: Example: Direct Mapped Cache (E = 1)
S = 2s sets
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 109: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
block offset
tag

## Slide 110: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
int (4 Bytes) is here
block offset
No match: old line is evicted and replaced

## Slide 111: Direct-Mapped Cache Simulation
M=16 byte addresses, B=2 bytes/block,
S=4 sets, E=1 Blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
x
t=1
s=2
b=1
xx
x
0
?
?
v
Tag
Block
miss
1
0
M[0-1]
hit
miss
1
0
M[6-7]
miss
1
1
M[8-9]
miss
1
0
M[0-1]
Set 0
Set 1
Set 2
Set 3

## Slide 112: A Higher Level Example
int sum_array_rows(double a[16][16])
{
int i, j;
double sum = 0;
for (i = 0; i < 16; i++)
for (j = 0; j < 16; j++)
sum += a[i][j];
return sum;
}
32 B = 4 doubles
assume: cold (empty) cache,
a[0][0] goes here
int sum_array_cols(double a[16][16])
{
int i, j;
double sum = 0;
for (j = 0; j < 16; j++)
for (i = 0; i < 16; i++)
sum += a[i][j];
return sum;
}
blackboard
Ignore the variables sum, i, j

## Slide 113: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 114: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
tag

## Slide 115: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
short int (2 Bytes) is here
No match:
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …

## Slide 116: 2-Way Set Associative Cache Simulation
M=16 byte addresses, B=2 bytes/block,
S=2 sets, E=2 blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
xx
t=2
s=1
b=1
x
x
0
?
?
v
Tag
Block
0
0
0
miss
1
00
M[0-1]
hit
miss
1
01
M[6-7]
miss
1
10
M[8-9]
hit
Set 0
Set 1

## Slide 117: A Higher Level Example
int sum_array_rows(double a[16][16])
{
int i, j;
double sum = 0;
for (i = 0; i < 16; i++)
for (j = 0; j < 16; j++)
sum += a[i][j];
return sum;
}
32 B = 4 doubles
assume: cold (empty) cache,
a[0][0] goes here
int sum_array_cols(double a[16][16])
{
int i, j;
double sum = 0;
for (j = 0; j < 16; j++)
for (i = 0; i < 16; i++)
sum += a[i][j];
return sum;
}
blackboard
Ignore the variables sum, i, j

## Slide 118: Full Associative Caches

## Slide 119: Advantages & Disadvantages
Direct Mapped Cache
Set Associative Cache
Full Associative Caches

## Slide 120: What about writes?
Multiple copies of data exist:
  L1, L2, Main Memory, Disk
What to do on a write-hit?
  Write-through (write immediately to memory)
  Write-back (defer write to memory until replacement of line)
    Need a dirty bit (line different from memory or not)
What to do on a write-miss?
  Write-allocate (load into cache, update line in cache)
    Good if more writes to the location follow
  No-write-allocate (writes immediately to memory)
Typical
  Write-through + No-write-allocate
  Write-back + Write-allocate

## Slide 121: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way,
  Access: 11 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 30-40 cycles
Block size: 64 bytes for all caches.

## Slide 122: Cache Performance Metrics
Miss Rate
  Fraction of memory references not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (in percentages):
    3-10% for L1
    can be quite small (e.g., < 1%) for L2, depending on size, etc.

## Slide 123: Cache Performance Metrics
Hit Time
  Time to deliver a line in the cache to the processor
    includes time to determine whether the line is in the cache
  Typical numbers:
    1-2 clock cycle for L1
    5-20 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    typically 50-200 cycles for main memory (Trend: increasing!)

## Slide 124: Let‘s think about those numbers
Huge difference between a hit and a miss
  Could be 100x, if just L1 and main memory
Would you believe 99% hits is twice as good as 97%?
  Consider: cache hit time of 1 cycle miss penalty of 100 cycles
  Average access time:
  97% hits: 1 cycle + 0.03 * 100 cycles = 4 cycles
  99% hits: 1 cycle + 0.01 * 100 cycles = 2 cycles
This is why “miss rate” is used instead of “hit rate”

## Slide 125: Writing Cache Friendly Code
Make the common case go fast
  Focus on the inner loops of the core functions
Minimize the misses in the inner loops
  Repeated references to variables are good (temporal locality)
  Stride-1 reference patterns are good (spatial locality)
Key idea: Our qualitative notion of locality is quantified through our understanding of cache memories.

## Slide 126: 6.2 Cache
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 127: The Memory Mountain
Read throughput (read bandwidth)
  Number of bytes read from memory per second (MB/s)
Memory mountain: Measured read throughput as a function of spatial and temporal locality.
  Compact way to characterize memory system performance.

## Slide 128: Memory Mountain Test Function
/* The test function */
void test(int elems, int stride) {
int i, result = 0;
volatile int sink;
for (i = 0; i < elems; i += stride)
result += data[i];
sink = result; /* So compiler doesn't optimize away the loop */
}
/* Run test(elems, stride) and return read throughput (MB/s) */
double run(int size, int stride, double Mhz)
{
double cycles;
int elems = size / sizeof(int);
test(elems, stride); /* warm up the cache */
cycles = fcyc2(test, elems, stride, 0); /* call test(elems,stride) */
return (size / stride) / (cycles / Mhz); /* convert cycles to MB/s */
}

## Slide 129: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12 | s13 | s14 | s15 | s16 | s32 | s64
64M | 4029.59 | 2752.75 | 2159.29 | 1710.75 | 1391.48 | 1176.29 | 1015.77 | 890.72 | 845.57 | 805.46 | 773.78 | 757.94 | 727.91 | 712.66 | 705.63 | 701.98 | 598.19 | 601.22
32M | 4029.36 | 2752.39 | 2160.62 | 1710.98 | 1391.5 | 1176.54 | 1016.71 | 891.8 | 846.98 | 807.22 | 775.18 | 760.41 | 730.74 | 714.98 | 709.26 | 708.88 | 608.99 | 607.39
16M | 4040.1 | 2788.42 | 2188.92 | 1742.97 | 1421.69 | 1201.31 | 1038.37 | 911.7 | 870.39 | 835.31 | 809.25 | 798.05 | 780.28 | 778.37 | 787.2 | 744.13 | 633.53 | 608.86
8M | 4374.01 | 3610.74 | 3002.03 | 2492.39 | 2131.04 | 1821.71 | 1564.14 | 1414.18 | 1404.78 | 1408.59 | 1423.67 | 1456.86 | 1499.61 | 1600.13 | 1667.47 | 1231.7 | 1078.97 | 1026.03
4M | 4642.47 | 4583.8 | 4074.93 | 3557.51 | 3337.59 | 2898.78 | 2535.22 | 2248.83 | 2227.41 | 2203.98 | 2187.29 | 2164.18 | 2156.96 | 2148.52 | 2146.83 | 2131.36 | 2038.29 | 2060.87
2M | 4674.06 | 4659.06 | 4153.1 | 4016.4 | 3540.78 | 3027.05 | 2625.06 | 2321.73 | 2306.4 | 2292.86 | 2282.38 | 2270.35 | 2264.14 | 2259.8 | 2260.46 | 2261.54 | 2224.92 | 2431.58
1M | 4673.77 | 4656.98 | 4156.32 | 4012.65 | 3535.85 | 3021.82 | 2623.08 | 2318.19 | 2303.72 | 2291.55 | 2280.42 | 2270.24 | 2264.82 | 2261.86 | 2261.31 | 2271.41 | 2237.27 | 2432.74
512K | 4673 | 4658.05 | 4267.3 | 4052.55 | 3730.88 | 3236.67 | 2839.93 | 2527.15 | 2513.25 | 2503.12 | 2494.19 | 2517.44 | 2523.1 | 2551.67 | 2555.53 | 2477.41 | 2420.17 | 2590.64
256K | 4672.31 | 4645.58 | 4300.1 | 4091.3 | 3890.2 | 3175.38 | 2748.26 | 2351.27 | 2518.38 | 2627.49 | 2644.71 | 2646.45 | 2690.79 | 2715.46 | 2762.7 | 2445.48 | 2440.11 | 2560.87
128K | 4669.89 | 4661.44 | 4661.75 | 4570.55 | 4453.42 | 4070.1 | 3626.17 | 2349.05 | 3332.47 | 3318.78 | 3328.21 | 3312.1 | 3351.75 | 3197.56 | 3342.59 | 3330.51 | 3335.4 | 3374.9
64K | 4664.69 | 4647.96 | 4646.51 | 4575.1 | 4473.68 | 4218.51 | 3642.61 | 3334.78 | 3395.82 | 3398 | 3403.08 | 3411.87 | 3395.99 | 3299.01 | 4287.45 | 3416.74 | 3389.13 | 3374.16
32K | 4654.62 | 4624.5 | 4631.69 | 4615.62 | 4600.39 | 4585.6 | 4572.8 | 4809.1 | 4803.13 | 4789.7 | 4790.97 | 4784.65 | 4754.23 | 4768.54 | 4750.25 | 4742.01 | 6545.16 | 6408.41
Intel Core i7
32 KB L1 i-cache
32 KB L1 d-cache
256 KB unified L2 cache
8M unified L3 cache
All caches on-chip

## Slide 130: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12 | s13 | s14 | s15 | s16 | s32 | s64
64M | 4029.59 | 2752.75 | 2159.29 | 1710.75 | 1391.48 | 1176.29 | 1015.77 | 890.72 | 845.57 | 805.46 | 773.78 | 757.94 | 727.91 | 712.66 | 705.63 | 701.98 | 598.19 | 601.22
32M | 4029.36 | 2752.39 | 2160.62 | 1710.98 | 1391.5 | 1176.54 | 1016.71 | 891.8 | 846.98 | 807.22 | 775.18 | 760.41 | 730.74 | 714.98 | 709.26 | 708.88 | 608.99 | 607.39
16M | 4040.1 | 2788.42 | 2188.92 | 1742.97 | 1421.69 | 1201.31 | 1038.37 | 911.7 | 870.39 | 835.31 | 809.25 | 798.05 | 780.28 | 778.37 | 787.2 | 744.13 | 633.53 | 608.86
8M | 4374.01 | 3610.74 | 3002.03 | 2492.39 | 2131.04 | 1821.71 | 1564.14 | 1414.18 | 1404.78 | 1408.59 | 1423.67 | 1456.86 | 1499.61 | 1600.13 | 1667.47 | 1231.7 | 1078.97 | 1026.03
4M | 4642.47 | 4583.8 | 4074.93 | 3557.51 | 3337.59 | 2898.78 | 2535.22 | 2248.83 | 2227.41 | 2203.98 | 2187.29 | 2164.18 | 2156.96 | 2148.52 | 2146.83 | 2131.36 | 2038.29 | 2060.87
2M | 4674.06 | 4659.06 | 4153.1 | 4016.4 | 3540.78 | 3027.05 | 2625.06 | 2321.73 | 2306.4 | 2292.86 | 2282.38 | 2270.35 | 2264.14 | 2259.8 | 2260.46 | 2261.54 | 2224.92 | 2431.58
1M | 4673.77 | 4656.98 | 4156.32 | 4012.65 | 3535.85 | 3021.82 | 2623.08 | 2318.19 | 2303.72 | 2291.55 | 2280.42 | 2270.24 | 2264.82 | 2261.86 | 2261.31 | 2271.41 | 2237.27 | 2432.74
512K | 4673 | 4658.05 | 4267.3 | 4052.55 | 3730.88 | 3236.67 | 2839.93 | 2527.15 | 2513.25 | 2503.12 | 2494.19 | 2517.44 | 2523.1 | 2551.67 | 2555.53 | 2477.41 | 2420.17 | 2590.64
256K | 4672.31 | 4645.58 | 4300.1 | 4091.3 | 3890.2 | 3175.38 | 2748.26 | 2351.27 | 2518.38 | 2627.49 | 2644.71 | 2646.45 | 2690.79 | 2715.46 | 2762.7 | 2445.48 | 2440.11 | 2560.87
128K | 4669.89 | 4661.44 | 4661.75 | 4570.55 | 4453.42 | 4070.1 | 3626.17 | 2349.05 | 3332.47 | 3318.78 | 3328.21 | 3312.1 | 3351.75 | 3197.56 | 3342.59 | 3330.51 | 3335.4 | 3374.9
64K | 4664.69 | 4647.96 | 4646.51 | 4575.1 | 4473.68 | 4218.51 | 3642.61 | 3334.78 | 3395.82 | 3398 | 3403.08 | 3411.87 | 3395.99 | 3299.01 | 4287.45 | 3416.74 | 3389.13 | 3374.16
32K | 4654.62 | 4624.5 | 4631.69 | 4615.62 | 4600.39 | 4585.6 | 4572.8 | 4809.1 | 4803.13 | 4789.7 | 4790.97 | 4784.65 | 4754.23 | 4768.54 | 4750.25 | 4742.01 | 6545.16 | 6408.41
Intel Core i7
32 KB L1 i-cache
32 KB L1 d-cache
256 KB unified L2 cache
8M unified L3 cache
All caches on-chip
Slopes 斜坡 of
spatial
locality

## Slide 131: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12 | s13 | s14 | s15 | s16 | s32 | s64
64M | 4029.59 | 2752.75 | 2159.29 | 1710.75 | 1391.48 | 1176.29 | 1015.77 | 890.72 | 845.57 | 805.46 | 773.78 | 757.94 | 727.91 | 712.66 | 705.63 | 701.98 | 598.19 | 601.22
32M | 4029.36 | 2752.39 | 2160.62 | 1710.98 | 1391.5 | 1176.54 | 1016.71 | 891.8 | 846.98 | 807.22 | 775.18 | 760.41 | 730.74 | 714.98 | 709.26 | 708.88 | 608.99 | 607.39
16M | 4040.1 | 2788.42 | 2188.92 | 1742.97 | 1421.69 | 1201.31 | 1038.37 | 911.7 | 870.39 | 835.31 | 809.25 | 798.05 | 780.28 | 778.37 | 787.2 | 744.13 | 633.53 | 608.86
8M | 4374.01 | 3610.74 | 3002.03 | 2492.39 | 2131.04 | 1821.71 | 1564.14 | 1414.18 | 1404.78 | 1408.59 | 1423.67 | 1456.86 | 1499.61 | 1600.13 | 1667.47 | 1231.7 | 1078.97 | 1026.03
4M | 4642.47 | 4583.8 | 4074.93 | 3557.51 | 3337.59 | 2898.78 | 2535.22 | 2248.83 | 2227.41 | 2203.98 | 2187.29 | 2164.18 | 2156.96 | 2148.52 | 2146.83 | 2131.36 | 2038.29 | 2060.87
2M | 4674.06 | 4659.06 | 4153.1 | 4016.4 | 3540.78 | 3027.05 | 2625.06 | 2321.73 | 2306.4 | 2292.86 | 2282.38 | 2270.35 | 2264.14 | 2259.8 | 2260.46 | 2261.54 | 2224.92 | 2431.58
1M | 4673.77 | 4656.98 | 4156.32 | 4012.65 | 3535.85 | 3021.82 | 2623.08 | 2318.19 | 2303.72 | 2291.55 | 2280.42 | 2270.24 | 2264.82 | 2261.86 | 2261.31 | 2271.41 | 2237.27 | 2432.74
512K | 4673 | 4658.05 | 4267.3 | 4052.55 | 3730.88 | 3236.67 | 2839.93 | 2527.15 | 2513.25 | 2503.12 | 2494.19 | 2517.44 | 2523.1 | 2551.67 | 2555.53 | 2477.41 | 2420.17 | 2590.64
256K | 4672.31 | 4645.58 | 4300.1 | 4091.3 | 3890.2 | 3175.38 | 2748.26 | 2351.27 | 2518.38 | 2627.49 | 2644.71 | 2646.45 | 2690.79 | 2715.46 | 2762.7 | 2445.48 | 2440.11 | 2560.87
128K | 4669.89 | 4661.44 | 4661.75 | 4570.55 | 4453.42 | 4070.1 | 3626.17 | 2349.05 | 3332.47 | 3318.78 | 3328.21 | 3312.1 | 3351.75 | 3197.56 | 3342.59 | 3330.51 | 3335.4 | 3374.9
64K | 4664.69 | 4647.96 | 4646.51 | 4575.1 | 4473.68 | 4218.51 | 3642.61 | 3334.78 | 3395.82 | 3398 | 3403.08 | 3411.87 | 3395.99 | 3299.01 | 4287.45 | 3416.74 | 3389.13 | 3374.16
32K | 4654.62 | 4624.5 | 4631.69 | 4615.62 | 4600.39 | 4585.6 | 4572.8 | 4809.1 | 4803.13 | 4789.7 | 4790.97 | 4784.65 | 4754.23 | 4768.54 | 4750.25 | 4742.01 | 6545.16 | 6408.41
Intel Core i7
32 KB L1 i-cache
32 KB L1 d-cache
256 KB unified L2 cache
8M unified L3 cache
All caches on-chip
Slopes of
spatial
locality
Ridges 山脊 of
Temporal
locality

## Slide 132: 6.2 Cache
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 133: An Case Study

## Slide 134: Discussion
How do you define the “locality” ?
How to tune your program ?
How does the locality affect our caches?

## Slide 135: Miss Rate Analysis for Matrix Multiply
Assume:
  Line size = 32B (big enough for four 64-bit words)
  Matrix dimension (N) is very large
    Approximate 1/N as 0.0
  Cache is not even big enough to hold multiple rows
Analysis Method:
  Look at access pattern of inner loop
A
k
i
B
k
j
C
i
j

## Slide 136: Matrix Multiplication Example
Description:
  Multiply N x N matrices
  O(N3) total operations
  N reads per source element
  N values summed per destination
    but may be able to hold in register
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
Variable sum
held in register

## Slide 137: Layout of C Arrays in Memory (review)
C arrays allocated in row-major order
  each row in contiguous memory locations
Stepping through columns in one row:
  for (i = 0; i < N; i++)
    sum += a[0][i];
  accesses successive elements
Stepping through rows in one column:
  for (i = 0; i < n; i++)
    sum += a[i][0];
  accesses distant elements
  no spatial locality!

## Slide 138: Rearranging loops

## Slide 139: Three kinds of Matrix Multiplication
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}

## Slide 140: Which is the fastest ? Why ?
Guess ?
  ijk
  ikj
  kij
  kji
  jki
  jik

## Slide 141: Matrix Multiplication (ijk)
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Column-
wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.25 1.0 0.0

## Slide 142: Matrix Multiplication (jik)
/* jik */
for (j=0; j<n; j++) {
for (i=0; i<n; i++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Row-wise
Column-
wise
Fixed
Misses per inner loop iteration:
  A B C
  0.25 1.0 0.0

## Slide 143: Matrix Multiplication (kij)
/* kij */
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.0 0.25 0.25

## Slide 144: Matrix Multiplication (ikj)
/* ikj */
for (i=0; i<n; i++) {
for (k=0; k<n; k++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.0 0.25 0.25

## Slide 145: Matrix Multiplication (jki)
/* jki */
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Column-
wise
Column-
wise
Fixed
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0

## Slide 146: Matrix Multiplication (kji)
/* kji */
for (k=0; k<n; k++) {
for (j=0; j<n; j++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Fixed
Column-
wise
Column-
wise
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0

## Slide 147: Core i7 Matrix Multiply Performance
Chart: Array size (n)
| 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750
jki | 6.4 | 6.87 | 4.14 | 5.53 | 10.93 | 33.23 | 49.43 | 51.49 | 52.06 | 52.06 | 52.07 | 52.09 | 52.12 | 52.17 | 52.2
kji | 6.4 | 6.82 | 4.01 | 5.33 | 11.04 | 33.21 | 49.42 | 51.5 | 52.07 | 52.08 | 52.09 | 52.1 | 52.14 | 52.19 | 52.23
ijk | 5.31 | 6.35 | 6.29 | 3.7 | 3.72 | 3.71 | 3.72 | 3.83 | 4.6 | 7.74 | 11.71 | 16.54 | 20.57 | 23.85 | 23.86
jik | 5.4 | 6.23 | 3.64 | 3.71 | 3.61 | 3.6 | 3.63 | 3.74 | 4.64 | 7.57 | 11.62 | 16.44 | 20.44 | 23.68 | 23.66
kij | 4.37 | 5.36 | 3.23 | 3.32 | 3.29 | 3.24 | 3.2 | 3.17 | 3.16 | 3.14 | 3.13 | 3.12 | 3.1 | 3.1 | 3.08
ikj | 3.58 | 5.31 | 3.19 | 3.18 | 3.15 | 3.12 | 3.1 | 3.1 | 3.11 | 3.09 | 3.07 | 3.06 | 3.02 | 3.02 | 3.01
jki / kji
ijk / jik
kij / ikj

## Slide 148: Concluding Observations
Programmer can optimize for cache performance
  How data structures are organized
  How data are accessed
    Nested loop structure
    Blocking is a general technique
All systems favor “cache friendly code”
  Getting absolute optimum performance is very platform specific
    Cache sizes, line sizes, associativities, etc.
  Can get most of the advantage with generic code
    Keep working set reasonably small (temporal locality)
    Use small strides (spatial locality)

## Slide 149: 6.3 Virtual Memory
Address spaces
VM as a tool for caching
VM as a tool for memory management
VM as a tool for memory protection
Address translation

## Slide 150: A System Using Physical Addressing
Used in “simple” systems like embedded microcontrollers in devices like cars, elevators, and digital picture frames
0:
1:
M-1:
Main memory
CPU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data word
8:
...
4

## Slide 151: A System Using Virtual Addressing
Used in all modern servers, desktops, and laptops
One of the great ideas in computer science
0:
1:
M-1:
Main memory
MMU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data word
8:
...
CPU
Virtual address
(VA)
CPU Chip
4
4100

## Slide 152: Address Spaces
Linear address space: Ordered set of contiguous non-negative integer addresses: {0, 1, 2, 3 … }
Virtual address space: Set of N = 2n virtual addresses {0, 1, 2, 3, …, N-1}
Physical address space: Set of M = 2m physical addresses {0, 1, 2, 3, …, M-1}

## Slide 153: Why Virtual Memory (VM)?
Uses main memory efficiently
  Use DRAM as a cache for the parts of a virtual address space
Simplifies memory management
  Each process gets the same uniform linear address space
Isolates address spaces
  One process can’t interfere with another’s memory
  User program cannot access privileged kernel information (Really ?? Think over an example that you can be a hacker)

## Slide 154: Today
Address spaces
VM as a tool for caching
VM as a tool for memory management
Address translation

## Slide 155: VM as a Tool for Caching
Virtual memory is an array of N contiguous bytes stored on disk.
The contents of the array on disk are cached in physical memory (DRAM cache)
  These cache blocks are called pages (size is P = 2p bytes)
PP 2m-p-1
Physical memory
Empty
Empty
Uncached
VP 0
VP 1
VP 2n-p-1
Virtual memory
Unallocated
Cached
Uncached
Unallocated
Cached
Uncached
PP 0
PP 1
Empty
Cached
0
N-1
M-1
0
Virtual pages (VPs)
stored on disk
Physical pages (PPs)
cached in DRAM

## Slide 156: DRAM Cache Organization
DRAM cache organization driven by the enormous miss penalty
  DRAM is about 10x slower than SRAM
  Disk is about 10,000x slower than DRAM
Consequences
  Large page (block) size: typically 4-8 KB, sometimes 4 MB
  Fully associative
    Any VP can be placed in any PP
    Requires a “large” mapping function – different from CPU caches
  Highly sophisticated, expensive replacement algorithms
    Too complicated and open-ended to be implemented in hardware

## Slide 157: Page Tables
A page table is an array of page table entries (PTEs) that maps virtual pages to physical pages.
  Per-process kernel data structure in DRAM
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3

## Slide 158: Page Hit
Page hit: reference to VM word that is in physical memory (DRAM cache hit)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 159: Page Fault
Page fault: reference to VM word that is not in physical memory (DRAM cache miss)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 160: Handling Page Fault
Page miss causes page fault (an exception)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 161: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 162: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 163: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
Offending instruction is restarted: page hit!
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 164: Locality to the Rescue Again!
Virtual memory works because of locality
At any point in time, programs tend to access a set of active virtual pages called the working set
  Programs with better temporal locality will have smaller working sets
If (working set size < main memory size)
  Good performance for one process after compulsory misses
If ( SUM(working set sizes) > main memory size )
  Thrashing: Performance meltdown where pages are swapped (copied) in and out continuously

## Slide 165: Today
Address spaces
VM as a tool for caching
VM as a tool for memory management
VM as a tool for memory protection
Address translation

## Slide 166: VM as a Tool for Memory Management
Key idea: each process has its own virtual address space
  It can view memory as a simple linear array
  Mapping function scatters addresses through physical memory
    Well chosen mappings simplify memory allocation and management
Virtual Address Space for Process 1:
Physical
Address
Space (DRAM)
0
N-1
(e.g., read-only
library code)
Virtual Address Space for Process 2:
VP 1
VP 2
...
0
N-1
VP 1
VP 2
...
PP 2
PP 6
PP 8
...
0
M-1
Address
translation

## Slide 167: VM as a Tool for Memory Management
Memory allocation
  Each virtual page can be mapped to any physical page
  A virtual page can be stored in different physical pages at different times
Sharing code and data among processes
  Map virtual pages to the same physical page (here: PP 6)
Virtual Address Space for Process 1:
Physical
Address
Space (DRAM)
0
N-1
(e.g., read-only
library code)
Virtual Address Space for Process 2:
VP 1
VP 2
...
0
N-1
VP 1
VP 2
...
PP 2
PP 6
PP 8
...
0
M-1
Address
translation

## Slide 168: Today
Address spaces
VM as a tool for caching
VM as a tool for memory management
VM as a tool for memory protection
Address translation

## Slide 169: VM Address Translation
Virtual Address Space
  V = {0, 1, …, N–1}
Physical Address Space
  P = {0, 1, …, M–1}
Address Translation
  MAP: V  P U {}
  For virtual address a:
    MAP(a) = a’ if data at virtual address a is at physical address a’ in P
    MAP(a) =  if data at virtual address a is not in physical memory
      Either invalid or stored on disk

## Slide 170: Summary of Address Translation Symbols
Basic Parameters
  N = 2n : Number of addresses in virtual address space
  M = 2m : Number of addresses in physical address space
  P = 2p : Page size (bytes)
Components of the virtual address (VA)
  TLBI: TLB index
  TLBT: TLB tag
  VPO: Virtual page offset
  VPN: Virtual page number
Components of the physical address (PA)
  PPO: Physical page offset (same as VPO)
  PPN: Physical page number
  CO: Byte offset within cache line
  CI: Cache index
  CT: Cache tag

## Slide 171: Address Translation With a Page Table
Virtual page number (VPN)
Virtual page offset (VPO)
Physical page number (PPN)
Physical page offset (PPO)
Virtual address
Physical address
Valid
Physical page number (PPN)
Page table base register
(PTBR)
Page table
Page table address
for process
Valid bit = 0:
page not in memory
(page fault)
0
p-1
p
n-1
0
p-1
p
m-1

## Slide 172: Address Translation: Page Hit
1) Processor sends virtual address to MMU
2-3) MMU fetches PTE from page table in memory
4) MMU sends physical address to cache/memory
5) Cache/memory sends data word to processor
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5

## Slide 173: Address Translation: Page Fault
1) Processor sends virtual address to MMU
2-3) MMU fetches PTE from page table in memory
4) Valid bit is zero, so MMU triggers page fault exception
5) Handler identifies victim (and, if dirty, pages it out to disk ? Otherwise )
6) Handler pages in new page and updates PTE in memory
7) Handler returns to original process, restarting faulting instruction
MMU
Cache/
Memory
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5
Disk
Page fault handler
Victim page
New page
Exception
6
7

## Slide 174: Integrating VM and Cache
VA
CPU
MMU
PTEA
PTE
PA
Data
Memory
PA
PA
miss
PTEA
PTEA
miss
PTEA
hit
PA
hit
Data
PTE
L1
cache
CPU Chip
VA: virtual address, PA: physical address, PTE: page table entry, PTEA = PTE address

## Slide 175: Speeding up Translation with a TLB
Page table entries (PTEs) are cached in L1 like any other memory word
  PTEs may be evicted by other data references
  PTE hit still requires a small L1 delay
Solution: Translation Lookaside Buffer (TLB)
  Small hardware cache in MMU
  Maps virtual page numbers to physical page numbers
  Contains complete page table entries for small number of pages

## Slide 176: TLB Hit
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
4
5
A TLB hit eliminates a memory access
TLB
VPN
3

## Slide 177: TLB Miss
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
5
6
TLB
VPN
4
PTEA
3
A TLB miss incurs an additional memory access (the PTE) Fortunately, TLB misses are rare. Why?

## Slide 178: Summary
Programmer’s view of virtual memory
  Each process has its own private linear address space
  Cannot be corrupted by other processes
System view of virtual memory
  Uses memory efficiently by caching virtual memory pages
    Efficient only because of locality
  Simplifies memory management and programming

## Slide 179: Memory Summary
Memory Hierarchy
  DRAM
  Disk
Cache
  Direct Mapped Cache
  Set Mapped Cache
Virtual Memory
  MMU

## Slide 180: Relationship
Registers
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
cheaper
per byte
Remote secondary storage
(tapes, distributed file systems, Web servers)
Local disks hold files retrieved from disks on remote network servers
Main memory holds disk blocks retrieved from local disks
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from L2 cache
CPU registers hold words retrieved from L1 cache
L2 cache holds cache lines retrieved from main memory
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
costlier
per byte

## Slide 181: Group Homework(1~2 people)
Suppose you are playing a computer game (e.g. Warcraft, StarCraft, FiFa 2015 …), use all you have learnt to explain the data transforming & processing process. You should try to write down all the details you think that is essential for you to play games.

## Slide 182: Group Homework(1~2 people)
The followings should be covered.
Storage: Disk or SSD, Main Memory, Virtual Memory, Cache, Register.
Processor: Instructions, Register Files, Pipeline, ALU
Print & Submit this homework on the last lesson (Dec. 16th)

## Slide 183: Homework
Review Chapter 6, Chapter 9
Practice Problem 9.1-9.3
Practice Problem 6.1-6.14
Submit this homework on the last lesson (Dec. 16th)
Preview COMPUTER RGANIZATION AND ARCHITECTURE DESIGNING FOR PERFORMANCE Chapter 7

## Slide 184: Thank You