## Slide 1: Computer Organization Principles
School of Software, Dalian University of Technology
Chi Lin (林驰)
chilin@mail.dlut.edu.cn

## Slide 2: System Bus
Definitions
Categories
Feature & Characteristics
Bus Architecture

## Slide 3: Definition of Bus
Necessity
  Complicated
  Lack of scalability
English
French
Russian
Japanese
Chinese
Notes: 分散连接的复杂性，规则性、可扩展性都不好，效率低下

## Slide 4: Basic Notations of Bus
Necessity
English
French
Russian
Japanese
Chinese
Chinese
Notes: 分散连接的复杂性，规则性、可扩展性都不好，效率低下

## Slide 5: Definition of Bus
In computer architecture, a bus (from the Latin omnibus, meaning "for all") is a communication system that transfers data between components inside a computer, or between computers. This expression covers all related hardware components (wire, optical fiber, etc.) and software, including communication protocols.

## Slide 6: Characteristic
Multiple receiver
Only one sender

## Slide 7: Examples: CPU oriented bus system architecture 的 双 总 线 结 构
CPU
I/O Bus
M
Bus
Memory
I/O Interface
I/O
Device 1
I/O
Device 2
…
…
I/O
Device n
I/O Interface
I/O Interface

## Slide 8: Advantages & Disadvantages
Adv.
  Convenient
Dis.
  Increase CPU burden
  Low CPU efficiency

## Slide 9: Example：Single Bus Architecture
System Bus
CPU
Memory
I/O Interface
I/O
Dev1
I/O
Dev2
I/O Interface
…
I/O
Dev3
I/O Interface
…

## Slide 10: Memory oriented dual bus architecture
System bus
Memory
CPU
I/O Interface
I/O
Dev 1
…
I/O
Dev n
I/O Interface
…
Memory
Bus

## Slide 11: Category of buses
On-chip bus
  On board, cache register
System bus
  Processor, memory, I/O information transforming
  Triple bus：Data Bus, Address bus, Control bus
Communication bus
Computer to computer, computer to other devices

## Slide 12: Examples: On-chip bus (Internal Bus)
On-chip bus
CPU
cache
CPU

## Slide 13: System bus (Triple bus)

## Slide 14: Example: Communication Bus
Computer
Computer
Dev 1
Dev 2
Communication bus

## Slide 15: System bus
Data bus
  Bi-directional data transmission
  The number of bits of the data bus is called the data bus width
CPU
Mem
data bus
8

## Slide 16: Address bus
Single directional bus
For specifying the location of the memory unit in the memory or I/O devices.
How to determine the bits of the address bus
CPU
存储器
address bus
？

## Slide 18: 2、地址总线
The number of bits of the address bus is related to the number of the unit.
E.g. Given n address lines, how many memory unit are there in the memory.
Byte addressing
256B memory capacity, how many address lines?
2KB …
16MB…
4GB…
Notes: 类比门牌地址

## Slide 19: Control Bus
Transmit control signals
One direction
E.g.
  Reset, Clock, Interrupt, Bus request, memory read & write, I/O read & write….
CPU
Mem/External Dev
control bus

## Slide 20: Communication bus
Definition
For communication between computers, computers and devices.
Features
  Transmission speed is inversely proportional to distance
Types：Serial, Parallel Port

## Slide 21: Serial Communication
One bit by one bit (一位一位顺序依次传输)
Short range, low cost
8 times transmission for one byte
  MSB：Most Significant Bit
  LSB：Least Significant Bit
Notes: RS-485接口的最大传输距离标准值为4000英尺，实际上可达 3000米，另外RS-232-C接口在总线上只允许连接1个收发器，即单站能力。而

## Slide 22: Example IIC Bus
Notes: I2C(Inter－Integrated Circuit)总线是一种由PHILIPS公司开发的两线式串行总线，用于连接微控制器及其外围设备。I2C总线产生于在80年代，最初为音频和视频设备开发，如今主要在服务器管理中使用，其中包括单个组件状态的通信。例如管理员可对各个组件进行查询，以管理系统的配置或掌握组件的功能状态，如电源和系统风扇。可随时监控内存、硬盘、网络、系统温度等多个参数，增加了系统的安全性，方便了管理。

## Slide 23: Parallel communication
Multiple bits are transmitted simultaneously on the data bus lines from the source
Less than 30 meters
Faster that serial transmission
Notes: 类比门牌地址

## Slide 24: Features of Buses
CPU
Memory
I/O
Other boards
BUS
Mainboard

## Slide 25: Bus Architecture
Unibus 单总线
Multibus 多总线
  Double 双总线
  Triple 三总线
  Four buses 四总线

## Slide 26: Unibus Architecture
CPU
Mem
I/O Interface
I/O
Dev 1
I/O
Dev 2
I/O Interface
…
I/O
Dev n
I/O Interface
…
Simple structure, easy to scale, low speed, bottleneck

## Slide 27: Multibus Architecture
Bus Manager
I/O INF
Dev n
…
…
I/O INF
Dev 0
CPU
Main Mem
Main Memory Bus
I/O Bus
Double bus
Low speed devices are separated from main memory bus.

## Slide 28: Triple Bus Architecture
Main Mem
bus
DMA Bus
I/O Bus
CPU
Memory
Dev
Dev
High Speed Dev
I/O INF
I/O INF
I/O INF
…
…
Main memory bus is used for information exchange between CPU and main memory. I/O bus is used for transmit information between CPU and I/O devices. DMA bus is responsible for the data delivering between main memory and I./O devices.

## Slide 29: Example 2: Triple Bus
LAN
System Bus
CPU
Cache
Local bus
Extend BI
Extended Bus
Modem
Serial INF
SCSI
Local I/O controller
Memory
The local bus is used to connect between processor and cache.
The extended bus interface is used to connect with the I/O devices.

## Slide 30: Four bus architecture
MM
Modem
Memory
EBI
LAN
SCSI
CPU
Serial bus
FAX
System bus
Local bus
High speed bus
Extended bus
Graphical Dev
Cache/bridge
Based on the characteristics, especially the execution speed, devices are divided into two levels. High speed devices are connected with the high speed I/O bus. Low speed devices are connected to the extended bus.

## Slide 31: Bus Control
Conflicting
Bus selection
Communication Control

## Slide 32: Chain query mode
Bus
Control
Unit
I/O INF 0
…
BS
BR
I/O接口1
I/O INF n
…
BG
DB
AD
BS －Bus Busy
BR－Bus Request
BG－Bus Agree
I/O INF 1
Easy to connect and scale, insensitive to faulty, no priority

## Slide 33: Counter Query Model
0
BS －Bus Busy
BR－Bus Request
Bus
Control
Unit
AB
DB
I/O INF 0
…
BS
BR
I/O接口1
I/O INF n
Dev Addr
I/O INF 1
Counter
1
Insensitive to faulty. Increase device addresses, complicated control

## Slide 34: Independent Query
排队器
Queue
Bus
Control
Unit
DB
AB
I/O INF0
I/O INF1
I/O INF n
…
BR0
BG0
BR1
BG1
BRn
BGn
BG－Bus Agree
BR－Bus Request
Fast response, flexible priority control, complex logical, massive control buses

## Slide 35: I/O Usage
The computer system’s I/O architecture is its interface to the outside world. This architecture provides a systematic means of controlling interaction with the outside world and provides the operating system with the information it needs to manage I/O activity effectively.

## Slide 36: I/O Category
The are three principal I/O techniques:
  programmed I/O(程序查询方式), in which I/O occurs under the direct and continuous control of the program requesting the I/O operation;
interrupt-driven I/O(中断), in which a program issues an I/O command and then continues to execute, until it is interrupted by the I/O hardware to signal the end of the I/O operation;
direct memory access (DMA), in which a specialized I/O processor takes over control of an I/O operation to move a large block of data.

## Slide 37: I/O Module
Each module interfaces to the system bus or central switch and controls one or more peripheral devices (外设).
An I/O module is not simply a set of mechanical connectors that wire a device into the system bus. Rather, the I/O module contains logic for performing a communication function between the peripheral and the bus.

## Slide 38: Discussion
Is the system bus directly connected to the peripherals ? Why ?
A) Yes B) No

## Slide 39: Peripherals
Peripherals do not directly connect to the system bus, the reasons are:
Variety
Data transfer rate
Data formats

## Slide 40: I/O Module is needed
I/O has two major functions
Interface to the processor and memory via the system bus or central switch
Interface to one or more peripheral devices by tailored data links

## Slide 42: External Devices
An external device attaches to the computer by a link to an I/O module
The link is used to exchange control, status, and data between the I/O module and the external device.
An external device connected to an I/O module is often referred to as a peripheral device or, simply, a peripheral.

## Slide 43: External devices
Human readable: Suitable for communicating with the computer user
Machine readable: Suitable for communicating with equipment
Communication: Suitable for communicating with remote devices

## Slide 44: External Devices
Keyboard
Disk
…

## Slide 45: I/O Modules
The major functions or requirements for an I/O module fall into the following categories:
Control and timing
Processor communication
Device communication
Data buffering
Error detection

## Slide 46: Control and Timing
The processor interrogates the I/O module to check the status of the attached device.
The I/O module returns the device status.
If the device is operational and ready to transmit, the processor requests the transfer of data, by means of a command to the I/O module.
The I/O module obtains a unit of data (e.g., 8 or 16 bits) from the external device.
The data are transferred from the I/O module to the processor.

## Slide 47: Processor communication
Command decoding: The I/O module accepts commands from the processor, typically sent as signals on the control bus. For example, an I/O module for a disk drive might accept the following commands: READ SECTOR, WRITE SECTOR, SEEK track number, and SCAN record ID. The latter two commands each include a parameter that is sent on the data bus.
Data: Data are exchanged between the processor and the I/O module over the data bus.

## Slide 48: Processor communication
Status reporting: Because peripherals are so slow, it is important to know the status of the I/O module. For example, if an I/O module is asked to send data to the processor (read), it may not be ready to do so because it is still working on the previous I/O command. This fact can be reported with a status signal. Common status signals are BUSY and READY. There may also be signals to report various error conditions.
Address recognition: Just as each word of memory has an address, so does each I/O device. Thus, an I/O module must recognize one unique address for each peripheral it controls.

## Slide 49: I/O Module Structure

## Slide 50: Functionality of I/O module
I/O module components
  Device select lines
  Data lines
  Command lines
  Status lines
I/O INF
Dev
I/O INF
Dev
Data lines
Command lines
Status lines
I/O Bus
Device Select lines

## Slide 51: I/O module organization
Cmd Reg
Cmd Decoder
Chip Select
Circuit
Device Status
Mark
Data Buffer
Register
Control Logic Circuit
I/O Module
External Dev
DB
Cmd
Stat
DB
CB
SB
CPU
AB

## Slide 52: I/O techniques
Programmed I/O
Interrupt-driven I/O
Direct memory access (DMA)
I/O channel & I/O processor

## Slide 53: Programmed I/O
Dev
Dev
Dev

## Slide 54: Interrupt-driven
Dev
Dev
Dev

## Slide 55: DMA
Dev
Dev
Dev
DMA

## Slide 56: I/O Channels
Dev
Dev
DMA
Channel

## Slide 57: I/O Processors
Dev
Dev
DMA
I/O Processors

## Slide 58: Programmed I/O
With programmed I/O, data are exchanged between the processor and the I/O module.
The processor executes a program that gives it direct control of the I/O operation, including sensing device status, sending a read or write command, and transferring the data. When the processor issues a command to the I/O module, it must wait until the I/O operation is complete.

## Slide 59: Interrupt-driven I/O
With interrupt-driven I/O, the processor issues an I/O command, continues to execute other instructions, and is interrupted by the I/O module when the latter has completed its work.

## Slide 60: DMA
The alternative is known as direct memory access (DMA). In this mode, the I/O module and main memory exchange data directly, without processor involvement.

## Slide 61: Discuss the Advs and Disadvs.
Programmed I/O
Interrupt driven I/O
DMA

## Slide 62: Comparison

## Slide 64: Programmed I/O
When the processor is executing a program and encounters an instruction relating to I/O, it executes that instruction by issuing a command to the appropriate I/O module.

## Slide 65: Programmed I/O
With programmed I/O, the I/O module will perform the requested action and then set the appropriate bits in the I/O status register.
  The I/O module takes no further action to alert the processor.
  In particular, it does not interrupt the processor.
Thus, it is the responsibility of the processor periodically to check the status of the I/O module until it finds that the operation is complete.

## Slide 66: Four types of I/O commands
Control: Used to activate a peripheral and tell it what to do. For example, a magnetic-tape unit may be instructed to rewind or to move forward one record. These commands are tailored to the particular type of peripheral device.
Test: Used to test various status conditions associated with an I/O module and its peripherals. The processor will want to know that the peripheral of interest is powered on and available for use. It will also want to know if the most recent I/O operation is completed and if any errors occurred.

## Slide 67: Four types of I/O commands
Read: Causes the I/O module to obtain an item of data from the peripheral and place it in an internal buffer. The processor can then obtain the data item by requesting that the I/O module place it on the data bus.
Write: Causes the I/O module to take an item of data (byte or word) from the data bus and subsequently transmit that data item to the peripheral.

## Slide 68: I/O Instructions
There is a close correspondence between the I/O-related instructions that the processor fetches from memory and the I/O commands that the processor issues to an I/O module to execute the instructions
That is, the instructions are easily mapped into I/O commands, and there is often a simple one-to-one relationship. The form of the instruction depends on the way in which external devices are addressed.

## Slide 69: I/O command
When the processor issues an I/O command, the command contains the address of the desired device.
Thus, each I/O module must interpret the address lines to determine if the command is for itself.

## Slide 70: I/O Addressing
Memory-mapped I/O (统一编址)：a single address space for memory locations and I/O devices.
  10 address lines for 2^10 memory units and I/O devices
Isolated I/O(独立编址)：The full range of addresses may be available for both. Specialized I/O instructions are used.
  10 address lines for 2^10 memory units and 2^10 devices respectively.

## Slide 71: Programmed I/O
Test Stat 1
Dev 1
Ready?
Test Stat N
Dev N
Ready?
…
Run Dev 1
Y
N
N
Run Dev N
Y
Flowchart
Test Stat
Exchange data
Ready?
Y
N
Single-Dev
Multi-Dev
Test cmd
Transfer
ctrl
Transfer
cmd

## Slide 72: A Program
Set init addr of mem buf
Set counter
Start dev
Transmit a word
Revise addr
Revise counter
Terminate I/O
Ready？
Finish？
N
Y
Y
N
Send a word

## Slide 73
②
Dev select circuit
DBR
Q
Q
&
DB
Ready
Start
cmd
AB
SEL
Input data
Start
dev
Finish
①
③
④
⑤
⑥
D
B
①
②
③
⑤
1
0
1
0
④
⑥
Circuit of Programmed I/O: Input
CPU
Dev

## Slide 74: Interrupted driven I/O
The problem with programmed I/O is that the processor has to wait a long time for the I/O module of concern to be ready for either reception or transmission of data. The processor, while waiting, must repeatedly interrogate the status of the I/O module. As a result, the level of the performance of the entire system is severely degraded.

## Slide 75: Interrupted driven I/O
An alternative is for the processor to issue an I/O command to a module and then go on to do some other useful work.
The I/O module will then interrupt the processor to request service when it is ready to exchange data with the processor.
The processor then executes the data transfer, as before, and then resumes its former processing.

## Slide 76: An example: Input
For input, the I/O module receives a READ command from the processor.
The I/O module then proceeds to read data in from an associated peripheral.
Once the data are in the module’s data register, the module signals an interrupt to the processor over a control line.
The module then waits until its data are requested by the processor. When the request is made, the module places its data on the data bus and is then ready for another I/O operation.

## Slide 77: Printing
Send INT REQ
Idle
RCV
Data
Rcv
Data
Device
Send INT REQ
Print
Print
Printer
Main Pro
Resume
Resume
Response to INT
INT Return
Response to INT
INT Return
Start
Printer
SEND
Data
Transmit
Data
CPU

## Slide 78: Discuss
When the processor is executing instructions and a interrupt occurs, what do you think the execution procedure?
Which information should be well-saved ?

## Slide 79: Hardware & Software Interrupt
In systems programming, an interrupt is a signal to the processor emitted by hardware or software indicating an event that needs immediate attention.
An interrupt alerts the processor to a high-priority condition requiring the interruption of the current code the processor is executing.
The processor responds by suspending its current activities, saving its state, and executing a function called an interrupt handler (or an interrupt service routine, ISR) to deal with the event. This interruption is temporary, and, after the interrupt handler finishes, the processor resumes normal activities.

## Slide 80: Interrupt Handler
In computer systems programming, an interrupt handler, also known as an interrupt service routine or ISR, is a callback function in microcontroller firmware, an operating system or a device driver, whose execution is triggered by the reception of an interrupt. In general, interrupts and their handlers are used to handle high-priority conditions that require the interruption of the current code the processor is executing.

## Slide 81: Interrupt Processing
The device issues an interrupt signal to the processor.

## Slide 82: Interrupt Processing
The processor finishes execution of the current instruction before responding to the interrupt.

## Slide 83: Interrupt Processing
The processor tests for an interrupt, determines that there is one, and sends an acknowledgment signal to the device that issued the interrupt. The acknowledgment allows the device to remove its interrupt signal.

## Slide 84: Interrupt Processing
The processor now needs to prepare to transfer control to the interrupt routine.
To begin, it needs to save information needed to resume the current program at the point of interrupt. The minimum information required is (a) the status of the processor, which is contained in a register called the program status word (PSW), and (b) the location of the next instruction to be executed, which is contained in the program counter. These can be pushed onto the system control stack.

## Slide 85: Interrupt Processing
At this point, the program counter and PSW relating to the interrupted program have been saved on the system stack.

## Slide 86: Interrupt Processing
The processor now loads the program counter with the entry location of the interrupt-handling program that will respond to this interrupt.

## Slide 87: Interrupt Processing
The interrupt handler next processes the interrupt. This includes an examination of status information relating to the I/O operation or other event that caused an interrupt. It may also involve sending additional commands or acknowledgments to the I/O device.

## Slide 88: Interrupt Processing
When interrupt processing is complete, the saved register values are retrieved from the stack and restored to the registers.

## Slide 89: Interrupt Processing
The final act is to restore the PSW and program counter values from the stack. As a result, the next instruction to be executed will be from the previously interrupted
program.

## Slide 91: Advs & Disadvs
Interrupt I/O is more efficient than programmed I/O because it eliminates needless waiting.
However, interrupt I/O still consumes a lot of processor time, because every word of data that goes from memory to I/O module or from I/O module to memory must pass through the processor.

## Slide 92: Interrupt Execution
Priority
Preemptive

## Slide 93: Sequential interrupt processing

## Slide 94: Multiple interrupt

## Slide 95: Multiple Interrupt

## Slide 96: Drawbacks of Programmed and Interrupt-Driven I/O
The I/O transfer rate is limited by the speed with which the processor can test and service a device.
The processor is tied up in managing an I/O transfer; a number of instructions must be executed for each I/O transfer.
When large volumes of data are to be moved, a more efficient technique is required: direct memory access (DMA).

## Slide 97: DMA (Memory  I/O)
DMA involves an additional module on the system bus.
DMA module must use the bus only when the processor does not need it, or it must force the processor to suspend operation temporarily. (DMA模块需要使CPU挂起一段时间)
The latter technique is more common and is referred to as cycle stealing, because the DMA module in effect steals a bus cycle.(DMA周期窃取技术)

## Slide 98: DMA Technique
When the processor wishes to read or write a block of data, it issues a command to the DMA module, by sending to the DMA module the following information:
  read or write control line between the processor and the DMA module.
  the address of the I/O device
  the starting location
  the number of words to be read or written

## Slide 99: Working process of DMA
The processor then continues with other work. It has delegated this I/O operation to the DMA module. The DMA module transfers the entire block of data, one word at a time, directly to or from memory, without going through the processor.
When the transfer is complete, the DMA module sends an interrupt signal to the processor.
Thus, the processor is involved only at the beginning and end of the transfer

## Slide 100: Instruction Cycles

## Slide 101: Feature of DMA
Interrupt signal is used but it is not an interrupt procedure
  the processor does not save a context
  the processor pauses for one bus cycle
Think over some other techniques that pause one cycle.

## Slide 102: Homework
List three broad classifications of external, or peripheral, devices.
What are the major functions of an I/O module?
List and briefly define three techniques for performing I/O.
What is the difference between memory-mapped I/O and isolated I/O?
When a DMA module takes control of a bus, and while it retains control of the bus, what does the processor do?

## Slide 103: Thank You